## Slide 1: geometry scans performed for the same Spray M and “single-hole atomizer” with the same ball and build
Spray G
Spray M
Moon, Powell (APS, above).
6.00 mm
1.459 mm
CT imaging at MS St
Credit: Kyungwon Lee and Joonsik Hwang
Single-Hole Atomizer
SHA #730
CT imaging at Argonne APS
Credit: Chi Moon and Chris Powell
Spray M #755
full serial number 038450BA0411213755PL
Provided to Sandia (Pickett) for initial analysis

## Slide 2
Orifice inlet is very sharp – laser machined. Spray G made by EDM
Analysis after some rotation and centering:
Notes: D:\xray\sha\aps\sprayM_Slice.m

## Slide 3: new recommended settings for Spray M Lagrangian simulations
Spray G
Spray M
No 3D CFD mesh/geometry available yet
Mesh and STL files available at
https://ecn.sandia.gov/gasoline-spray-combustion/computational-method/mesh-and-geometry/
Notes: from plumeDefinitions.pptx

## Slide 4
Inlet radius to hole is very sharp – laser drilled
Coordinates are centered on sac and ball symmetry—hole is offset and canted by ~ 1.4 degrees
170 mm cylinder,
rotated 1.4°
Hole is barely convergent:
Measure a 1.08 degree full angle convergence, or a K factor = (d_inlet – d_outlet) / 10 mm = 0.3
CT imaging at APS
Credit Chris Powell and Chi Moon
Notes: Adding analysis from Argonne x-ray experiments for same hole. See D:\xray\sha\aps\shaSlice.m for figures

## Slide 5
Processed sac, hole, counterbore radius in Matlab. But “corrected” the hole to make it a perfect cylinder based upon original x-ray image on slide 1, and measured optical microscopy from Sandia and MS St. Using diameter of 0.170 mm for hole measured at Sandia. MS St measure 0.175 mm
Hole and counterbore are processed from STL with the hole “cleaned”, but I do not believe the reconstruction has the accuracy to render the hole inlet appropriately.
Orange line is wireframe used by Marco Arienti to create a triangular tessellation (FE mesh) of surface
Available for internal-flow simulations
Notes: D:\xray\sha\MSSTATE_ECN_INJ\pointSHA.m
figure(88) is a cut after some centering
Orange line (measured) is stored as
"D:\xray\sha\MSSTATE_ECN_INJ\ECN_single_hole\SHAwireframeRadiusMeasured.csv"