## Slide 1
First presented at ECN9.17 on 7 aug 2025, new edits:
Geometry of ECN-designated HDEV4 piezo injector for hydrogen research
Lyle Pickett, Bernice Mills, Steven Luna
Sandia National Laboratories CRF
Abdullah Zaihi, Hong Im, Moez Ben Houidi, William Roberts
KAUST
After performing 5.8 mm x-ray CT scans, kaust Provided STL file to Sandia
Sandia performed minor modifications On imported CONVERGE file to make it possible to translate the pintle to a closed position

## Slide 2
45° from image axis
Scan by Bernice Mills (Sandia) using Zeiss Versa 620 with 10 mm voxel resolution
0.025 mm slot
3.89 mm annulus
3.60 mm annulus
x-ray CT scans of HDEV4 injector
PN 0261500804
HDEV42
Notes: D:\xray\hdev4h2\scanThroughhdev4Inject.m

## Slide 3
Identifying the region of contact with seat
3.60 mm diameter is in contact with pintle (or below 10 um voxel resolution over ½ of diameter) when closed

## Slide 4
What happens in this region as the needle lifts?

## Slide 5: Needle motion measurements Wu 2025 (KAUST)
https://doi.org/10.1063/5.0252859
0.16 ms ramp
Using time-varying lift to compute theoretical flow limit, Wu et al. measured Cd = 0.8 with Pinj = 50 bar
~ 54 mm lift
Notes: https://doi.org/10.4271/2025-01-8466, D:\xray\hdev4h2\theoreticalMdot.m shows A is 0.48 mm^2 at full lift

## Slide 6
flow will restrict at smaller diameter/annular opening
Minimum flow area is is actually a catenoid, not a cone!
https://math.stackexchange.com/questions/2930021/why-is-the-catenoid-the-minimal-surface-of-revolution
Using the smaller seat diameter has about a 10% effect on perceived flow area
flow already in divergent section at annulus exit
Notes: https://math.stackexchange.com/questions/2930021/why-is-the-catenoid-the-minimal-surface-of-revolution
D:\xray\hdev4h2\theoreticalMdot.m

## Slide 7
flow will restrict at smaller diameter/annular opening
Minimum flow area is is actually a catenoid, not a cone!
https://math.stackexchange.com/questions/2930021/why-is-the-catenoid-the-minimal-surface-of-revolution
Using the smaller seat diameter has about a 10% effect on perceived flow area
flow already in divergent section at annulus exit
STL file provided by KAUST (Zaihi & Im) at 54.4 mm lift height
Notes: https://math.stackexchange.com/questions/2930021/why-is-the-catenoid-the-minimal-surface-of-revolution
D:\xray\hdev4h2\theoreticalMdot.m

## Slide 8: Pintle lifted by 54.4 um with regions shown suitable for a moving valve simulation using CONVERGE
STL file provided by KAUST (Zaihi & Im) at 54.4 mm lift height
Small modifications by Luna and Pickett to define regions for pintle translation
Coordinate system with Z = 0 for closed injector
Region to stretch/compress during pintle motion
Notes: C:\pickett\ecn\h2hdev4lift54um

## Slide 9
annular area only 0.52 mm2
-> flow restriction upstream will restrict flow and cause pressure drop, from 50 bar to ~37bar
annular area only 0.52 mm2
flow area ~ 2.3 mm2
Notes: D:\xray\hdev4h2\scanThroughhdev4Inject.m, D:\xray\hdev4h2\theoreticalMdot.m
Used STEMS measurement of 1.2 g/s and can get this only with 37 bar upstream pressure

## Slide 10: rate of injection by Montanaro 2025, using 220V
ROI decrease during injection despite massive upstream volume
8 mm ID lines
https://doi.org/10.4271/2025-01-8466
This ROI must have had a higher lift height than 0.054 mm
Notes: https://doi.org/10.4271/2025-01-8466, D:\xray\hdev4h2\theoreticalMdot.m shows A is 0.48 mm^2 at full lift

## Slide 11: Status
HDEV4 Geometry/grid is provided to ECN participants for CFD simulations
  Lift height recommended for simulations is 0.0544 mm
  Smallest flow area not at exit of annulus
Significant restrictions exist inside the injector, with flow losses and decreasing pressure just upstream of valve seat

## Slide 12: acknowledgements
Sandia National Laboratories is a multi-mission laboratory managed and operated by National Technology and Engineering Solutions of Sandia, LLC, a wholly owned subsidiary of Honeywell International, Inc., for the U.S. Department of Energy’s National Nuclear Security Administration under contract DE-NA0003525.