## Slide 1: Experimental Databases on liquid Ammonia Non-reacting Spray from Spray M and G injector
Prof Christine Mounaïm-Rousselle & Ass Prof Camille Hespel
Thanks to Dr U. Sonawane
Université d’Orléans, INSA CVL, PRISME,, Orléans, France
christine.rousselle@univ-orleans.fr

## Slide 2: Physical properties of Ammonia
Lower density, lower viscosity
  Change on spray penetration
Properties | Ammonia | Gasoline | Diesel
Storage pressure at 300 K [bar] | 10.3 | 1 | 1
Density at 300 K [kg/m3] | 681 | 770 | 838.8
Viscosity at 298 K (µPa.s) | 131.7 | 529 | 3335
Surface tension (×10-3) [kg/s2] | 21.9 | 23.8 | 26
Boiling point at 1 atm [◦C] | -33.4 | 30-200 | 180-230
Latent heat of vaporization [kJ/kg] | 1369 | 71.78 | 47.86

## Slide 3: Physical properties of Ammonia
Lower density, lower viscosity
  Change on spray penetration
≠ surface tension =f(Tamb.)
  more pronounced droplet deformation during motion
  considerable impact on the spray dynamics and vaporization processes
Properties | Ammonia | Gasoline | Diesel
Storage pressure at 300 K [bar] | 10.3 | 1 | 1
Density at 300 K [kg/m3] | 681 | 770 | 838.8
Surface tension (×10-3) [kg/s2] | 21.9 | 23.8 | 26
Viscosity at 298 K (µPa.s) | 131.7 | 529 | 3335
Boiling point at 1 atm [◦C] | -33.4 | 30-200 | 180-230
Latent heat of vaporization [kJ/kg] | 1369 | 71.78 | 47.86
Properties | Ammonia | Gasoline | Diesel
Storage pressure at 300 K [bar] | 10.3 | 1 | 1
Density at 300 K [kg/m3] | 681 | 770 | 838.8
Viscosity at 298 K (µPa.s) | 131.7 | 529 | 3335
Surface tension (×10-3) [kg/s2] | 21.9 | 23.8 | 26
Boiling point at 1 atm [◦C] | -33.4 | 30-200 | 180-230
Latent heat of vaporization [kJ/kg] | 1369 | 71.78 | 47.86

## Slide 4: Physical properties of Ammonia
Lower density, lower viscosity
≠ surface tension =f(Tamb.)
Higher saturation vapor pressure
  high sensitivity to fuel temperature compared to other alternative fuels
  flash boiling phenomenon
Properties | Ammonia | Gasoline | Diesel
Storage pressure at 300 K [bar] | 10.3 | 1 | 1
Density at 300 K [kg/m3] | 681 | 770 | 838.8
Surface tension (×10-3) [kg/s2] | 21.9 | 23.8 | 26
Viscosity at 298 K (µPa.s) | 131.7 | 529 | 3335
Boiling point at 1 atm [◦C] | -33.4 | 30-200 | 180-230
Latent heat of vaporization [kJ/kg] | 1369 | 71.78 | 47.86
Properties | Ammonia | Gasoline | Diesel
Storage pressure at 300 K [bar] | 10.3 | 1 | 1
Density at 300 K [kg/m3] | 681 | 770 | 838.8
Viscosity at 298 K (µPa.s) | 131.7 | 529 | 3335
Surface tension (×10-3) [kg/s2] | 21.9 | 23.8 | 26
 | -33.4 | 30-200 | 180-230
 | 1369 | 71.78 | 47.86
Fuel

## Slide 5: experiments
What we need to do ?
Atomization process and fuel characteristics
  Effect on 'global' spray characteristics
  Effect on atomization (droplet size, distribution), volume of liquid
  Evaporation and Combustion

## Slide 6: experimental Considerations : our set-up
First set-up
Gauge control
He pressure
NH3 pressure
NH3
Tank
He
Tank
No injection pump for ammonia GDI injector
Pressurized with inert gas (He)
Advantages
Simple and cost-effective
Drawbacks
Mixing of Helium with NH3 ?
New set-up
NH3
Tank
Air pressure
NH3 Vent
NH3 In
Gauge control
Compressed air
Pump
Pneumatic Pressurizer (Maximator)
Advantages
No contamination
More precise
Drawbacks
Limitation in flow rate
Expensive
  (compatibility with NH3)
Dried air
NH3 hydrophyle !

## Slide 7: experimental Considerations : our set-up
Specificities of NH3 : hydroscopic
strong affinity for moisture (polarity and hydrogen bonding)
Absorbed water leads to formation of aqueous ammonia (NH4+)
Degradation of spray
Dried nitrogen or air
Specificities of NH3 : compatibility
Metal
No copper, nickel, brass + no alloys
'Problem' with Phinia injector :
Significant contamination on the ball/seat interface of various sizes (10 to 100µm)
Areas of cavitation erosion.
Specificities of NH3 : compatibility
Plastic and rubber
Prefer : Silicon Rubber (SR)
Possible :
Fluorated Tubber (FKM)
Natural Rubber (NR)
Avoid
Nitrile (NBR)
EPDM rubber (EPDM)
Chloroprene (CR)

## Slide 8: Needs to combine multiple techniques
Macroscopic and Near-field Schlieren

## Slide 9: Needs to combine multiple techniques
Macroscopic and Near-field Schlieren
Back Illumination Imaging
Temperature measurement
Fine thermocouple
Intrusive…Methods to be developped ?
Droplet size distribution ?

## Slide 10: experimental test conditions
Single Hole ECN GDI injector
Pinj. = 70b, Tamb. = 293K
Tfuel (°C) | Pamb (bar)
-10 | 0.5, 1, 3, 6
0 | 1, 3, 6
10 | 3
20 | 3
30 | 1,3
40 | 1
50 | 1
DBI test conditions
Schlieren test conditions
Tfuel (°C) | Pamb (bar)
-10 | 1, 2, 3, 4, 5
0 | 2
10 | 1, 2
20 | 1, 2, 4, 5, 7
30 | 1, 2, 3,
40 | 1, 2, 3
50 | 1, 2, 3, 4
Tfuel (°C) | Pamb (bar)
0, 20, 50 | 1, 3, 6
Droplet sizing by Particle Image Analyzer : 35 mm below injector top
Radial distance= 0 to 6 mm from centre
Tfuel (°C) | Pamb (bar)
0 | 1, 2, 3, 4, 5, 6
30 | 1, 2, 3, 4, 5, 6
-10, 0, 10, 20, 30, 40, 50 | 1
-10, 0, 10, 20, 30, 40, 50 | 3
ECN 8 holes SPRAY G

## Slide 11: Example of Spray morphology
Rp = 3.14
Rp = 9.64
Rp = 7.63
Rp = 5.72
Rp = 4.38
Rp = 1.53
Rp = 2.21
  Pamb = 2 bars, Tfuel= -10 - 50 °C
Rp>1 : flash boiling starts to occur !
Rp>6 spray width constant !
Near injector : ‘liquid’ chanel before atomization ?
Rp=Psat(Tfuel)/Pamb
Notes: Here, videos of the spray, are shown for a constant pressure of 2 bars
In this case, Rp varies from 1.5 to 9.6
_For all these cases flash boiling occurs.
_For a value of Rp from 1.5 to 5.7 the width of the spray increases then stabilizes for 7.6 and 9.6.
_We can also notice that the behavior near the injector becomes more pronounced as a function of Rp and we can observe, more easily at the level near the injector, a liquid tube and then the flaring of the spray. Phenomenon which does not appear for the conditions for non flashing conditions.

## Slide 12: Near field images
Red square = similar Rp (8-10)
  Different spray shapes !
Tfuel
Pamb.
Rp
Rp
Narrow spray =
no flash boiling mechanical break-up ?
Wide spray = flash boiling
Examples :
(0.3 bar, -10 °C) : less dense liquid core than (1 bar, 20 °C)
Less droplets ? Smaller droplets ? Very dense !!!
higher degree of flash boiling or evaporation ?

## Slide 13
'First Shocks' observed
Only for the extreme Rp of 68 to 203
(Pamb= 0.1 to 0.3 bar, Tfuel= 50 °C)
Schlieren set-up
  not sufficient sensitive ?
Mach disk formation, shock structures

## Slide 14
multiple injection bursts
Continuous liquid column
Diluted spray
Near field images
15 mm
4 mm

## Slide 15: Droplet sizing, distribution
Diffractometer : not possible in dense zone
  Small droplets, dense
PDPA : difficult in our vessel (optimised angle)
  Refraction index ?
Interferometric Laser Imaging for Droplet Sizing (ILIDS)
  Too dense = too droplet overlap
Particle Image Analyzer (PIA) ?
SLIPI ? Polarisation ratio ?
8 b
13 b
no Fb
Fb
Notes: Between the tank and combustion chamber the ammonia cross its saturation pressure inside the nozzle or outside.
In fact in the nozzle the pressure decrease between the injection pressure and combustion chamber pressure. The gradient eon pressure (Pinj and Pbacck) and also of lenght/Diameter ratio

## Slide 16
Near-field observation optics as an Optical microscope
Uniform and short-period backlight
35 mm below nozzle
radial distance (r) = x mm: from x−0.5 mm to x+0.5 mm
Particle Image Analyzer (PIA)
Pixel resolutions
x 2= 10.4 μm/px
x 5= 4.2 μm/px
x 10= 2.1 μm/px
Prof Hayakawa, Dr YR Chen
Tohoku University
10 images/conditions

## Slide 17
Particle Image Analyzer (PIA)
No measurement below 2µ !

## Slide 18
Particle Image Analyzer (PIA)

## Slide 19
Optical density
Collimated light illumination with Fourier Filtering

## Slide 20
Optical density
  OD < 1 Ballistic light dominating
  1 < OD < 2 Single scattering with the start of multiple light scattering
  OD > 2 : Multiple light scattering

## Slide 21
  Tackle multiple scattering issue
  Preserve modulated information
SLIPI Polarization Ratio
Prof E. Berrocal
Lund University

## Slide 22
Convergence of intensity for S-pol Component
Post-processing
  Quantification
    Possible
      average images (at least 80 !)
    Droplet sizing ?
      calibration needed

## Slide 23
Large number of finer droplets
Large number coarser droplets during injection
Sharper structure
Less dense spray
Blurred spray
Unclear structure
SLIPI -Polarization Ratio

## Slide 24
Υ
SLIPI -Polarization Ratio
Polarisation ratio = droplet sizing 'easier'/better than LIF/Mie
  S
  P

## Slide 25
Υ
Υ vs D21 calibration curve
Calibration
Polarization Ratio - droplet sizing ?

## Slide 26
Υ
Υ vs D21 calibration curve
Calibration
Droplet Diameter (D21) Distribution
3. Image Post Processing
3.4 Droplet diameter for ammonia flash boiling spray

## Slide 27
Tfuel = 20 °C
Pamb = 1 bar
Tfuel = -10 °C
Pamb = 6 bar
Droplet size distribution : need calibration !

## Slide 28: Liquid Ammonia injection
Everything have to be done
Atomisation : function of injector type geometry (L/D = 1 for Spray M), injection and ambiant conditions, …)
  Temperature, droplet sizing, velocity
Evaporation :
  Tamb variation
  NH3/air mixing : NH3 LIF, Raman ?
Combustion …
Both single and multi holes injectors
Complex spray /evaporation processes
Development of optical diagnostics
  Severe environments
  Strong flash boiling tendency
  Strong condensation tendency
    difficult experiments !

## Slide 29: Discharge coefficient
NTNU (T. Lovas group)
Multi-hole bassed = single hole
Pinj = 200 b
Datamatrix | Static Flow (g/s) | diam | Cd
Multi Holes injectors |  |  | 
038450BA0411213733PL | 11.767 | 1.70E-04 | 0.55
038450BA0411213750PL | 11.654 | 1.70E-04 | 0.55
038450BA0411213755PL | 11.686 | 1.70E-04 | 0.55
038450BA0411213756PL | 11.593 | 1.70E-04 | 0.54
038450BA0411213757PL | 11.485 | 1.70E-04 | 0.54
038450BA0411213770PL | 11.525 | 1.70E-04 | 0.54
038450BA0411213771PL | 11.679 | 1.70E-04 | 0.55
038450BA0411213772PL | 11.621 | 1.70E-04 | 0.54
038450BA0411213778PL | 11.68 | 1.70E-04 | 0.55
038450BA0411213779PL | 11.51 | 1.70E-04 | 0.54
Single Hole Injectors |  |  | 
038450BB0411213709PL | 1.657 | 1.70E-04 | 0.62
038450BB0411213715PL | 1.65 | 1.70E-04 | 0.62
038450BB0411213716PL | 1.656 | 1.70E-04 | 0.62
038450BB0411213730PL | 1.642 | 1.70E-04 | 0.61
038450BB0411213736PL | 1.646 | 1.70E-04 | 0.62
038450BB0411213746PL | 1.655 | 1.70E-04 | 0.62
038450BB0411213758PL | 1.649 | 1.70E-04 | 0.62
038450BB0411213759PL | 1.652 | 1.70E-04 | 0.62
038450BB0411213760PL | 1.642 | 1.70E-04 | 0.61
038450BB0411213773PL | 1.652 | 1.70E-04 | 0.62
Assessed under 100bar, with nHeptane |  | 
Measurement done injecting in a chamber without counterpressure |  | 
ECN GDI Injector

## Slide 30
Rp = 8.6
Tfuel = 20 °C
Pamb = 1 bar
Rp = 19.7
Tfuel = 50 °C
Pamb = 1 bar
400 µs
800 µs
1200 µs
1600 µs

## Slide 31
Rp = 8.6
Tfuel = 20 °C
Pamb = 1 bar
Rp = 19.7
Tfuel = 50 °C
Pamb = 1 bar
400 µs
800 µs
1200 µs
1600 µs