## Slide 1
Noud Maes (TU/e) n.c.j.maes@tue.nl
Moez Ben Houidi (KAUST) moez.benhouidi@outlook.com Alessandro Montanaro(STEMS) alessandro.montanaro@stems.cnr.it
ECN 10 workshop
Guidelines
Hydrogen Injection

## Slide 2: Hydrogen Injection (Low Pressure Direct Injection)
MOTIVATIONS
  Heavy-duty, off-road, & stationary applications are the main driver for hydrogen
  Better understanding of injection, mixture formation, and ignition of hydrogen DI
OBJECTIVES
  Investigate hydrogen injection processes using an injector with an outward-opening needle (ECN9 Bosch HDEV4, PN-0261500804) as the agreed baseline for both experimental and simulation work
  Focus on experiments and simulations to deepen the understanding of hydrogen injection and mixing dynamics
TARGET CONDITIONS
  Variations beyond the baseline are welcome; we will use these to refine testing conditions
  Access geometry, needle lift, and ROI details here https://ecn.sandia.gov/hydrogen/bosch-hdev-injector/
 | Pinj [bara] | Pamb [bara] | Ambient gas | Hydrogen Purity | T fuel & Tamb [K] | ET [ms] | Drive voltage [V]
Reference | 20 | 1 | N2 | >99.98% | ~298 | 2 | 160
Variations | 30, 50 | 2 | - | - | - | - | -

## Slide 3: Hydrogen Injection (Low Pressure Direct Injection)
INFORMATION OF INTEREST
  Injection and mixing data
    Experiments:
      mass flow rate, needle lift, injector geometry
      jet penetration, and area (line of sight Schlieren)
      mixing fields (local concentration, temperature, and velocity)
    Simulations:
      nozzle discharge/effective injection pressure
      jet penetration, and area (CFD Schlieren)
      time-resolved mixing-, temperature-, velocity-, and turbulence fields
DATA SUBMISSION
Preferred file format: MATLAB (.mat) or Excel (.xlsx) for processed data (e.g., jet penetration, area).
For 2D/3D data: a structured, evenly spaced grid format (e.g., matrix with fixed resolution in x, y, and z if applicable) helps ensure smooth comparisons:
  include axis references (units, origin) and resolution (e.g., grid spacing).
  adjust resolution to balance details and file size.
Optional: please share a short routine (MATLAB/Python) to demonstrate how to open and plot the data.

## Slide 4: Hydrogen Injection (single-hole orifice for LPDI)
TARGET CONDITIONS
  Typical Controlled Ignition engine conditions at BDC
    Follow standard HDEV4 test conditions
  Focus on single-hole orifice injection for LPDI configurations, differing from hollow cone injections (HDEV4).
INFORMATION OF INTEREST
  General overview: any available data or insights on ongoing activities
  Injection and mixing data
    Experiments:
      mass flow rate
      jet penetration, and area (line-of-sight Schlieren)
      mixing fields (local concentration, temperature, velocity, etc.)
    Simulations:
      nozzle discharge/effective injection pressure
      jet penetration, and area (line-of-sight CFD Schlieren)
      time-resolved mixing, temperature, velocity, and turbulence fields in the mid-plane
UNSW
KAUST (modified OEM 0261500109)
Sandia (ECN spray M)
TU/e (OEM 06F 906 036)
HDEV4 with cap (Rolke et al. doi: 10.3389/fmech.2022.868855)
Others?

## Slide 5
Hydrogen Injection (HIGH Pressure Direct Injection)
TARGET CONDITIONS
  Typical Compression Ignition engine TDC conditions
    Standard test conditions will be discussed in ECN10
INFORMATION OF INTEREST
  Any available information for general overview of activities is welcome?
  Injection and mixing data
    Experiments:
      mass flow rate
      jet penetration, and area (line-of-sight Schlieren)
      mixing fields (local concentration, temperature, velocity, etc.)
    Simulations:
      nozzle discharge/effective injection pressure
      jet penetration, and area (line-of-sight CFD Schlieren)
      time-resolved mixing, temperature, velocity, and turbulence fields in the mid-plane
  Auto-ignition, pilot ignition and flame structure data
    Experiments: Ignition delay, time-resolved OH* (or OH LIF, CH*, etc.)
    Simulations: Ignition delay, time-resolved species maps (H2, OH, NO, H2O)
UNSW
TU/e (OEM 06F 906 036)
KAUST (modified OEM 0261500109)
Sandia (ECN spray M)
TU/e (OEM 06F 906 036)
Others?