## Slide 1: Sustainable fuel compression-ignition combustion Julien manin & Daiana de leon
ECN 10 will take place in Chiba, Japan (near Tokyo)
  Date: December 14th and 15th
  Location: Chiba University
ECN 10 will take place right before COMODIA 2025, also in Chiba, Japan
  Dates: December 15th to 18th
  Location: Makuhari Messe International Conference Hall
ECN10 will focus on 5 different topical areas
  Hydrogen injection & combustion
  Sustainable fuel spark ignition
  Sustainable fuel compression-ignition combustion
  Ammonia injection and combustion
  Battery safety and thermal runaway

## Slide 2: Sustainable fuel compression-ignition combustion Julien manin & Daiana de leon
MOTIVATIONS
  Heavy-duty and off-road applications are the main drivers for CI combustion research
  Need to understand all aspects of CI combustion once the fuel is in the chamber
    Because this is the only session on CI combustion, it will cover the whole process from spray to emissions
  While we mostly focused on trying to understand what leads to the formation of pollutants before, the problem is different with alternative fuels where we need to understand the injection and combustion first
OBJECTIVES: Experimental and simulation data for comparisons
  Spray/injection and evaporation
  Mixing and additional mixing-related quantities
    Mild interest in fuel decomposition in case differences show up
  Ignition and flame stabilization
  Processes related to pollutant formation (NO, CO…)
  We anticipate little to no soot with these fuels, do the simulations confirm…?
TARGET CONDITIONS
  Injectors of interest: Spray D and Spray A-3
  Fuels: Methanol, ethanol, DME and OME, compared to reference n-dodecane
  Conditions: Spray A conditions (900 K, 15% O2, 150 MPa) with additional sweeps in temperature (MeOH/EtOH: 1200, 1100 & 1000 K - DME/OME: 1200, 1000, 800 & 1100 K), O2 (12 & 21%) and injection pressure (50 & 100 MPa) sweeps (in order of priority)

## Slide 3: Sustainable fuel compression-ignition combustion Julien manin & Daiana de leon
INFORMATION OF INTEREST
  Spray injection, evaporation and mixing
    Experiments: Time-resolved liquid length, vapor penetration and mixing fields
    Simulations: Droplet size, time-resolved liquid length, vapor penetration and fuel mixture fraction (report spray params.)
  Molecular breakdown (if possible)
    Simulations: Time-resolved main species maps (e.g. Fuel, C3H6, C2H6, C2H4, CH4)
  Ignition and flame stabilization and flame structure
    Experiments: Ignition delay, lift-off length, time-resolved CH2O LIF, OH* (or OH LIF, CH*, etc.)
    Simulations: Ignition delay, lift-off length, time-resolved CH2O and OH (OH* if available) maps (report chemistry/method)
  Pollutant formation
    Experiments: Given that we’re expecting little to no soot, it’s whatever we can get
    Simulations: Time-resolved map of pollutants NO, CO, aldehydes, or aromatics and soot maps if simulated
  Use ECN definitions for all experimental and numerical quantities
    https://ecn.sandia.gov/diesel-spray-combustion/computational-method/modeling-standards/
DATA SUBMISSION
Best file format is Matlab, but text or other mainstream formats like vtk OK
If possible, please send a quick routine as a guide on how to open and “plot” the data