## Slide 1
ECN4-Topic 10: Spray G in Engines
Guidance
Brian Peterson & Wei Zeng
brpeter@sandia.gov & wzeng@sandia.gov
Sandia National Laboratories

## Slide 2
50 us ASOI (-22.1 ᵒCA) 50 us ASOI (-18.0 ᵒCA)
100 us ASOI (-22.0 ᵒCA) 100 us ASOI (-17.4 ᵒCA)
150 us ASOI (-19.9 ᵒCA) 150 us ASOI (-16.8 ᵒCA)
200 us ASOI (-19.8 ᵒCA) 200 us ASOI (-16.2 ᵒCA)
250 us ASOI (-19.7 ᵒCA) 250 us ASOI (-15.6 ᵒCA)
300 us ASOI (-19.6 ᵒCA) 300 us ASOI (-15.0 ᵒCA)
350 us ASOI (-19.5 ᵒCA) 350 us ASOI (-14.4 ᵒCA)
400 us ASOI (-19.4 ᵒCA) 400 us ASOI (-13.8 ᵒCA)
450 us ASOI (-19.3 ᵒCA) 450 us ASOI (-13.2 ᵒCA)
500 us ASOI (-19.2 ᵒCA) 500 us ASOI (-12.6 ᵒCA)
550 us ASOI (-19.1 ᵒCA) 550 us ASOI (-12.0 ᵒCA)
600 us ASOI (-19.0 ᵒCA) 600 us ASOI (-11.4 ᵒCA)
650 us ASOI (-18.9 ᵒCA) 650 us ASOI (-10.6 ᵒCA)
700 us ASOI (-18.8 ᵒCA) 700 us ASOI (-10.0 ᵒCA)
750 us ASOI (-18.7 ᵒCA) 750 us ASOI (-9.4 ᵒCA)
800 us ASOI (-18.6 ᵒCA) 800 us ASOI (-8.8 ᵒCA)
850 us ASOI (-18.5 ᵒCA) 850 us ASOI (-8.2 ᵒCA)
900 us ASOI (-18.4 ᵒCA) 900 us ASOI (-7.6 ᵒCA)
950 us ASOI (-18.3 ᵒCA) 950 us ASOI (-7.0 ᵒCA)
SOI (-23 ᵒCA ATDC)
300 rpm
2000 rpm
At 2000 rpm, liquid jets quickly collapse and rotate with the swirl flow
Demonstrate the influence of intake-generated gas flow on spray development
Different from the spray in constant-volume chamber
Swirl flow direction
Motivation
  Spray development (late injection) in a DISI engine

## Slide 3
Experimental Objectives
The objective is to closely align engine efforts with that of Spray G in constant-volume chambers
Results will be used:
  to demonstrate and understand the influence of engine environment (BC’s, local flow, etc.) on spray development
  to compare with Spray G results obtained from measurements in constant-volume chambers
  to check the reproducibility of the measurements between facilities, operating conditions, injectors and engines (boundary conditions verification)
  as input data for model development

## Slide 4
Experimental conditions for Spray G
  Three experimental conditions for constant-volume chambers have been proposed by Spray G group
  The engines should be operated at timings (crank-angle) necessary to obtain thermodynamic environments that are similar to the Spray G conditions
Parameter Spray G Spray G2 Spray G3
Late injection Early injection Early injection
Flash boiling Non-flash-boiling
Fuel Iso-octane Iso-octane Iso-octane
Fuel pressure 20 Mpa 20 Mpa 20 MPa
Fuel temperature 90ᵒ C 90ᵒ C 90ᵒ C
Injector temperature 90ᵒ C 90ᵒ C 90ᵒ C
Ambient temperature 300ᵒ C 60ᵒ C 60ᵒ C
Ambient density 3.5 kg/m3 0.5 kg/m3 1.0 kg/m3
  (Pressure - Nitrogen) (600 kPa) (50 kPa) (100 kPa)
Injected quantity 10 mg 10 mg 10 mg
Number of injections 1 1 1

## Slide 5
Target of engine group for ECN4
  The primary goal is to finish early injection conditions before ECN4
    Spray G2 (flash-boiling) and G3
    A flat optical piston is recommended for early injection conditions
  Late injection is also recommended
    The guidance will be added shortly
Parameter Spray G Spray G2 Spray G3
Late injection Early injection Early injection
Flash boiling Non-flash-boiling
Fuel Iso-octane Iso-octane Iso-octane
Fuel pressure 20 Mpa 20 Mpa 20 MPa
Fuel temperature 90ᵒ C 90ᵒ C 90ᵒ C
Injector temperature 90ᵒ C 90ᵒ C 90ᵒ C
Ambient temperature 300ᵒ C 60ᵒ C 60ᵒ C
Ambient density 3.5 kg/m3 0.5 kg/m3 1.0 kg/m3
  (Pressure - Nitrogen) (600 kPa) (50 kPa) (100 kPa)
Injected quantity 10 mg 10 mg 10 mg
Number of injections 1 1 1

## Slide 6
Engine operation (proposed)
Operation parameters (similar to spray G2&G3)
  Fuel: iso-octane
  Injection pressure: 20 MPa / Central injection
  Coolant temperature: 90ᵒ C
  Oil temperature: 90ᵒ C
  Injection quantity: 10 mg
  Number of injections: 1
  Operation strategy: Motored operation with skip7-injection1*
    Operation strategy can be changed to keep the fuel temperature close to 90ᵒ C
Above-mentioned parameters for spray operation should be consistent for all groups
* To maintain fuel temperature for flash-boiling

## Slide 7
Engine operation (proposed)
Specific thermodynamic surroundings
  Average intake pressure: 50 kPa, 100 kPa
  Injection timing: Injection in early intake stroke
  (likely between -300° to 270 ° CA ATDC )
  but slightly different between groups
    In-cylinder pressure trace depends on engine
    Injection timing should be varied to ensure that the in-cylinder pressure is close to 50/100 kPa when fuel is injected. The flow effect is different for different CA, but this is unavoidable.
    For instance, Sandia DISI engine shows that the in-cylinder pressure of 50 kPa can be achieved around -300° to 270 ° CA ATDC when intake pressure is set to 50 kPa

## Slide 8
Engine operation (proposed)
Unique thermal surroundings
  Ambient temperature: 60 °C
    A heating facility is required to control the intake air temperature and the ambient temperature when fuel is injected.
    Normally, direct measurement of the ambient temperature is not straightforward. Therefore, estimation of ambient temperature at injection timing is recommended.
Unique flow dynamic environment
  Engine speed: 1000, 2000, 300 (recommended) rpm
    2000 rpm is preferable because it shows stronger flow impact on spray development
    Low engine speeds (300 rpm, thus weak flow effect) is recommended for comparison with near-quiescent constant-volume chamber measurements
  Flow generation: Unique (facility-specific)
    Stage of engine flow development will be different, but this is unavoidable
    On the other hand, it is useful to characterize the spray under various fluid dynamic environments (tumble, swirl, squish and turbulence level)
    Characterizing the in-cylinder gas flow generation is recommended

## Slide 9
Nozzle-hole labeling
Use electric connector to label the nozzle hole
Two possible relative locations
  The nozzle hole is labeled as 1, 2, 3 … 8.
  Approach: the closest hole is labeled as the first one.
Location 1:
Electric connector
1
2
3
4
6
5
7
8
Location 2:
Electric connector
1
2
3
4
6
5
7
8
The counterclockwise labeling direction is determined by looking at the injector tip

## Slide 10
Spray position
Position 1 is required, but position 2 is also recommended.
Position 1: one plume hits the spark plug (assume imaging through piston bowl window)
Position 2: spark plug is in between two plumes
Spray-plume
Spray-plume
Spark plug
Spark plug

## Slide 11
Diagnostics
The optical access for each engine is unique. Each group should consider appropriate techniques and camera views for spray measurements.
Here, the goal is to obtain the macro-spray development and vaporization in the engine, including
  Liquid-phase structure
    Mie-scattering (with head or side illumination) technique is recommended
  Vapor-phase structure
    Schlieren (if possible) or laser-induced-florescence (LIF) technique is recommended
  Quantified vapor concentration (recommended)
    PLIF technique is recommended (need further discussion, such as tracer)
Spray groups normally use simultaneous Schlieren and diffused back-illumination (or Mie-scattering) to get the liquid- and vapor-phase penetrations. This is recommended if possible.
PIV for flow characterization is recommended if possible.

## Slide 12
Data needed from experimentalists
Quantitative results (recommended)
  Imaging through optical cylinder: liquid and vapor penetrations vs. time
  Imaging through piston bowl window: liquid and vapor widths, and jet axial penetration (if applicable) vs. time
    For vapor width, full-width at half max in the mean concentration field is recommended
Flash-boiling normally causes spray collapse. Some specific definitions are recommended to quantify the collapse. (need further discussion)
Cyclic variation (due to flow variations) is a important nature for DISI engine. Quantification of spray variations from cycle-to-cycle is also recommended.
Pre-injection intake-induced gas flow generation (if any)

## Slide 13
Groups and potential start date
Experiments
  University of Michigan (Mohammad Fatouraie, Margaret Wooldridge)
    -Late October 2014 to Early January 2015
  Sandia DISI engine lab (Magnus Sjöberg)
    -Late January, 2015 (flexible)
  University of Duisburg-Essen (Sebastian Kaiser)
    -February, 2015
  TU Darmstadt (Benjamin Böhm)
    -April to June, 2015
  Shanghai Jiao Tong University (Min Xu, David Hung)
    -
  Sandia LTGC lab (John Dec) (Potential)
Simulation
  GM (Potential)

## Slide 14
Advertisement for simulation
It is important to examine your model under real engine conditions
Simulation for each of these three conditions is welcome.
Parameter Spray G Spray G2 Spray G3
Late injection Early injection Early injection
Flash boiling Non-flash-boiling
Fuel Iso-octane Iso-octane Iso-octane
Fuel pressure 20 Mpa 20 Mpa 20 MPa
Fuel temperature 90ᵒ C 90ᵒ C 90ᵒ C
Injector temperature 90ᵒ C 90ᵒ C 90ᵒ C
Ambient temperature 300ᵒ C 60ᵒ C 60ᵒ C
Ambient density 3.5 kg/m3 0.5 kg/m3 1.0 kg/m3
  (Pressure - Nitrogen) (600 kPa) (50 kPa) (100 kPa)
Injected quantity 10 mg 10 mg 10 mg
Number of injections 1 1 1

## Slide 15
Expectations for injector usage
As a user of an ECN Spray G injector, I agree to:
Ensure that my fuel system is clean and free of particles.
Use available Delphi “setup” injectors of the same type to ensure pressure and injector driver controls are functional, prior to installation of a Spray G injector.
Apply active cooling to the injector at all times to the target temperature to ensure that it does not overheat.
Prevent water condensation (and eventual rust/oxidation) and coking by purging of vessel with dry air or nitrogen.
Coating the nozzle with a light oil (or WD-40) after experiments are completed to prevent oxidation when in storage.
Measure ambient and injector temperature (and composition) boundary conditions to ensure that target conditions are met.
Provide relevant vessel or engine intake geometry to permit CFD simulation of the experiment.
Share results to the ECN archival website following instructions on the participation page.