## Slide 1: ECN5 Spray G Lagrangian Modeling Presenter: Lyle M. Pickett* Sandia National Laboratories *Sponsor: DOE Office of Vehicle Technologies Program managers: Gurpreet Singh & Leo Breton

## Slide 2
Contributors
Argonne National Laboratory
  Radiography/tomography measurements: Daniel Duke, Chris Powell, Katie Matusik, Alan Kastengren
General Motors R&D
  Rate of injection &
  Droplet velocity/sizing: Scott Parrish
Delphi
  Patternation: Lee Markle
Sandia National Laboratories
  High-speed PIV gas-phase velocity: Panos Sphicas (visiting from Imperial College), Scott Skeen, Lyle Pickett, Jonathan Frank
Argonne National Lab. (ANL)
  LES & RANS simulation, CONVERGE: Kaushik Saha, Sibendu Som
Politecnico di Milano (PoliMi)
  RANS simulation, Open-FOAM: Tommaso Lucchini, David Sinoir, Davide Paredi, Gianluca d’Errico
KAUST-Hong G. Im, F. E. Hernandez Perez
Wisconsin - Chris Rutland, Hongjiang Li
AramCo - Jihad A. Badra, Jaeheon Sim
  LES simulation, Open-FOAM
ETH-Zurich
  LES simulation, CD-Adapco: Lucas Zeugin, Yuri Wright
Modeling
Experiment

## Slide 3: Modeling Spray G via Lagrangian particle tracking is complex/difficult
37° Drill Angle
Plume cone
angle
Full outer spray half angle
Plume direction
37° drill angle
~33°
ECN4: courtesy Bizhan Befrui, Delphi
VOF simulation of internal flow
Major “knobs” of adjustment
  “Plume direction” angle relative to injector
  Individual plume “cone angle”

## Slide 4: Could/should we use simple measurements to specify plume direction and cone angle?
Plume vector redirection caused by BOTH internal flow and downstream fluid mechanics—patternation experiment at 1 atm not independent of aerodynamics
Plume direction and cone angle depend upon operating conditions
Emerging plume changes direction throughout injection
Delphi patternation at 1 atm:
z = 50 mm, Rplume= 33.2 mm
plume direction angle = 33°
plume cone angle, 90% mass = 17°
ECN4: UMass/GM

## Slide 5: Other challenging ways to get plume cone angle for Lagrangian simulations
Measure it using x-ray radiography
Model it using Eulerian-Eulerian internal flow
Simulations at counterbore exit
Argonne, Saha et al. SAE 2017-01-0834
Liquid vol
fraction
Argonne radiography
kg fuel / m3
Notes: Copied top from ECN4 presentation. Bottom images straight out of SAE paper

## Slide 6: Simulation contributions for ECN5
Can less-expensive simulations be used to define bc’s used later for more expensive simulations?
 | Polimi RANS | Argonne RANS | Argonne LES | KAUST-Aramco-UW LES | ETH-Zurich LES
Domain Dimensions | 169 x 248 mm | 108 x 108 mm | 108 x 108 mm | 100 x 60 x 60mm | 100 x 100 x 100mm
Base Cell Size | 4 mm | 1 mm | 1 mm | 1 mm | 2 mm
Min Cell Size | 1 mm | 0.125 mm | 0.125 mm | 0.5 mm | 0.125 mm
Nozzle tip included | No | No, Yes for one-way | No, Yes for one-way | Yes | Yes
Radial position of droplet parcel | 0.5 mm | 0.79 mm | 0.79 mm | 0.79 mm | 0.79 mm
Adaptive or Static Refinement | Adaptive | Both | Both | Both | Static
Cell Type | Cartesian & oriented | Cartesian cut-cell | Cartesian cut-cell | Cartesian | Cartesian
Total/Maximum Cell Count | 115,000 | 14 million | 14 million @ 1ms; 20 million @ 2ms | 2.2 million | 3.5 million
Number of spray parcels | 20k per plume | 400k per plume | 200k per plume | 200k per plume | 500K per plume
CPU cost | 1 realization 3 processors 40 minutes for 2 ms 2 CPU hrs for 2 ms | ? | 5 realizations 36 processors 10 hours for 1 ms 3600 CPU hrs for 2 ms | 5 realizations 32 processors 10 hours for 2 ms 1800 CPU hrs for 2 ms | 1 realization 96 processors 5 hours for 2 ms 480 CPU hrs for 2 ms

## Slide 7: Summary of models and setup
 | Polimi RANS | Argonne RANS | Argonne LES | KAUST-UW-Aramco LES | ETH-Zurich LES
CFD Code | OpenFOAM + Lib-ICE | CONVERGE | CONVERGE | OpenFOAM | Star-CD
Turbulence Model | Standard k-ε | Standard k-ε | LES – dynamic structure | LES dynamic structure with spray source/sink | LES – sub-grid k model
Injection Model | Lagrangian/Huh | Lagrangian/Blob | Lagrangian/Blob | Lagrangian/Blob | Lagrangian/Blob
Primary Break-up Model | Huh-Gosman | Kelvin-Helmholtz (KH) | Kelvin-Helmholtz (KH) | KH (Cb = 1.0, B1= 35) | Kelvin-Helmholtz (KH)
Secondary Break-up | Kelvin Helmholtz (KH) + Rayleigh Taylor (RT) | Rayleigh-Taylor (RT) | Rayleigh-Taylor (RT) | KH/RT competing | Rayleigh-Taylor (RT)
Vaporization | Spalding Number-based (mass-based) |  | Frössling | Frössling | Spalding Number-based (mass-based)
Heat Transfer | Ranz-Marshall |  | O’Rourke | Ranz-Marshall | Ranz-Marshall
Collision | None |  | NTC | None | O’Rourke
Droplet Drag | Dynamic without spherical correction |  | Dynamic | Dynamic without spherical correction | Standard
Initial gas turbulence | u’ = 1 m/s; Li = 2 mm |  | TKE=1.0; EPS=100.0 | TKE=7.9e-3 (35° PD) TKE = 1.6e-4(40° PD) | TKE=7.9e-3
Plume direction | 34°, 37° |  | 35° | 35°, 40° | 33°
Plume cone angle | Calculated from Huh-Gosman as 9° | 25°- 40°, “one-way” | 25°- 40°, “one-way” | 25°, 30°, 35°, 40° | 17°

## Slide 8
Simulation Setup – KAUST-UW-Aramco Group
CFD platform | Modified OpenFOAM 2.3.x
Fluid solver | sprayFoam (PISO algorithm)
Turbulence model | LES dynamic structure with spray source/sink term
Mesh | 2,111,968 Hexahedron cells (Static mesh refinement)
Typical CPU time | 10 hours using 32 processors
100 mm
60 mm
60 mm
∆ = 0.5 mm
∆ = 1.0 mm
The nozzle cutout is able to prevent gas flow entering the middle of spray from above the nozzle exit locations (N.E. Van Dam, Ph.D. Dissertation, University of Wisconsin-Madison, 2015)
Nozzle cutout
Cross-section: Octagon

## Slide 9
Simulation Setup – KAUST-UW-Aramco Group
Injection model | Lagrangian/Blob
Primary breakup | KH (Cb = 1.0, B1= 35)
Secondary breakup | KH/RT competing with each other
Vaporization | Frössling
Heat transfer | Ranz-Marshall
Collision | None
Droplet drag | Dynamic w/o non-spherical correction
Plume direction (°) | 35, 40
Plume cone angle (°) | 25, 30, 35, 40
Number of realizations | 5 (with different random number seed)
Initial TKE (m2/s2) | 7.9E-3 (for 35° PD), 1.6E-4 (for 40° PD)
Initial velocity (m/s) | 0
Injected fuel parcels | 80, 000
Injection velocity profile | Measured ROI
Hydraulic coefficients | CA = 0.69, CD =0.52 (from ECN 3 Topic 3.5)

## Slide 10: Animation of total mixture density at z=15 mm
Multiple realizations and average of all plumes used to generate statistics for comparison
ANL LES
35°Plume Direction / 35° Cone Angle
1 realization
KAUST-UW-AramCo LES
35°Plume Direction / 25° Cone Angle
Average of 5 realization
Notes: C:\pickett\ECN\mtgs\ECN5\topics\T9sprayGevap\scripts\argonneDensity15mmVideo.m C:\pickett\ECN\mtgs\ECN5\topics\T9sprayGevap\scripts\kwaDensity15mmVideo.m

## Slide 11: To qualify our CFD efforts as “predictive”, what experimental data is necessary (and available)?
Axial vapor penetration
  Schlieren measurements discussed by Daniel Vaquerizo, CMT
Axial liquid penetration
  Extinction imaging discussed by Daniel Vaquerizo, CMT
Plume liquid velocity
  Phase Doppler Interferometry measurements, Scott Parrish (GM)
Droplet size
  Phase Doppler Interferometry measurements, Scott Parrish (GM)
Gas-phase velocity between plumes
  High-speed PIV measurements discussed by Panos Sphicas (Imperial)
Plume direction and mass distribution
  X-ray radiography (z = 2,5,10 mm) as shown by Katie Matusik (ANL)
  Extinction imaging and PDI analysis
Will one simulation consistently “best match” all above?

## Slide 12: Start with evaluation of centerline z=15mm axial velocity
Central recirculation zone increases with higher plume direction, but does not meet level of experiment
PoliMi RANS
Plume direction _ Cone Angle
Notes: C:\share\Panos\Paper4-modelComparison\Tommaso\ECN5_results\extractw15.m.

## Slide 13: Almost immediate positive axial velocity with increased plume cone angle
Central recirculation zone increases with higher plume direction, but does not meet level of experiment
PoliMi RANS
Plume direction _ Cone Angle
Notes: C:\share\Panos\Paper4-modelComparison\Tommaso\ECN5_results\extractw15.m.

## Slide 14: KWA LES picks up central recirculation zone and merge of jets at end of injection
35 degree plume direction
Notes: C:\share\Panos\Paper4-modelComparison\Wisc\ECN5 Topic9 Results Submission-selected\w15plotUW.m

## Slide 15: KWA LES: Larger plume direction increases recirculation velocity
40 degree plume direction
Notes: C:\share\Panos\Paper4-modelComparison\Wisc\ECN5 Topic9 Results Submission-selected\w15plotUW.m

## Slide 16: Argonne LES: experiences a toggling/collapse with increased plume cone angle
35 degree plume direction
25° cone
z=15 mm
Mixture density
Notes: C:\share\Panos\Paper4-modelComparison\ANL\fig6_573.m

## Slide 17: ETH Zurich LES shows short-circuited recirculation
Plume direction/cone angle results appear specific to each implementation
Result is for a single LES realization
33° Plume direction, 17° cone angle
Notes: C:\share\Panos\Paper4-modelComparison\ETH\primaryViewMovie1.m

## Slide 18: RANS plume cone angles become more diffuse
ANL LES
35° Plume direction,
25° cone angle
Total mixture density
kg/m3
PoliMi RANS
34° Plume direction,
9° cone angle
Notes: Straight from paper

## Slide 19: RANS with high resolution also shows diffused mixing and probably collapse
25°
30°
35°
40°
“one-way”
Argonne RANS simulations
Saha et al. SAE 2017-01-0834
Argonne LES
35° Plume direction,
25° cone angle
Notes: Grabbed figure from SAE paper

## Slide 20: Total mixture density (fuel + gas)
Argonne simulations at z = 2 mm, 25° plume cone and 35° plume direction
Dashed line is measured plume center by Argonne x-ray (2.3 mm)
kg/m3
Notes: C:\pickett\ECN\mtgs\ECN5\topics\T9sprayGevap\scripts\mixingat2mm.m

## Slide 21: Near-nozzle geometry
Details about the nozzle tip affect simulation setup and axial datum
Notes: C:\pickett\ECN\mtgs\ECN5\topics\T9sprayGevap\scripts\mixingat2mm.m

## Slide 22: Adding axial offset reconciles the matter
Stated hole offset radius in simulation was 0.79 mm
Dashed line is assuming that Argonne used the hole exit as z = 0
Not the tip of the injector, as ECN convention
kg/m3
Notes: C:\pickett\ECN\mtgs\ECN5\topics\T9sprayGevap\scripts\mixingat2mm.m

## Slide 23: Argonne RANS shows delayed response, but more significant recirculation
Plume direction = 37°, Plume cone angle = 25°

## Slide 24: Liquid/gas velocity track together for KWA, not the case for PoliMi
Notes: C:\pickett\ECN\mtgs\ECN5\topics\T9sprayGevap\scripts\Velocity1.m

## Slide 25: ANL 35/35 shows better plume dispersion, but velocity higher than measured
Notes: C:\pickett\ECN\mtgs\ECN5\topics\T9sprayGevap\scripts\Velocity2.m

## Slide 26: Profiles of velocity, density, mixture fraction used to identify plume center
Nice agreement with measured liquid velocity
Plume center moves towards injector axis during injection
Measured liquid PDI velocity magnitude
Notes: C:\pickett\ECN\mtgs\ECN5\topics\T9sprayGevap\scripts\plumeMovementKW.m and C:\pickett\ECN\mtgs\ECN4\Topics\T9SprayGVessel\scripts\pdiVmag.m

## Slide 27: Larger plume direction is unrealistic
Some combinations of plume direction angle and cone angle provided decent fits to centerline gas velocity or penetration, but this practice cannot be justified when considering plume center
Notes: C:\pickett\ECN\mtgs\ECN5\topics\T9sprayGevap\scripts\plumeMovementKW40.m and

## Slide 28: Fuel re-entrainment between neighboring plumes
Total mixture density [kg/m3]
573K and 600 µs ASI
ANL LES, 35\25, 600 µs ASI
At this 9o rotation, the axial velocity is negative, providing recirculation towards the injector.
Mixture densities are significantly greater than the ambient density at this position, indicating that fuel mass is being transported upstream and into the recirculation zones beginning near the edges of the plumes.
Z = 15 mm
9°

## Slide 29: Simulated penetration scattered about experiment
Consistency when considering PIV gas-phase and PDI liquid-phase velocity (35\25)
But tuning to penetration yields a different solution (35\35 or 40\30)
Notes: C:\pickett\ECN\mtgs\ECN5\topics\T9sprayGevap\scripts\vaporKW.m

## Slide 30: Droplet size (SMD) predictions show radial variance, while the experiment is generally flat
Experiment shows spikes in SMD at EOI—but model does not show this.
Notes: C:\pickett\ECN\mtgs\ECN5\topics\T9sprayGevap\scripts\smdKW.m

## Slide 31: Effect of ambient temperature reveals weakness in current modeling
Sphicas SAE 2017-01-0837, with LES simulations by Argonne and RANS simulations by PoliMi
Trend opposite of experiment

## Slide 32: Modeling need-vaporization dynamics
Very different response to increased ambient temperature
Higher total mixture density because of vaporization cooling
ANL LES 35/25, PoliMi 34/9

## Slide 33: Current weaknesses
Experiments
  Have not provided quantitative vapor/liquid in “mixed” regions
  Radiography limited to non-vaporizing conditions
CFD (Lagrangian)
  Generally, RANS simulations appear to have difficulties resolving inter-plume fluid mechanics
  Do not consider that plume direction (moving out of the nozzle) changes with time
    consider that small- and multi-injection cycles are common
  Appear to have widely varying vaporization predictions
  Do not predict large SMD at EOI

## Slide 34: Overall observations
Will one simulation consistently “best match” all available experimental data?
  Sort of. Good consistency for (1) PDI liquid velocity, (2) PIV gas-phase velocity, (3) plume center identification via extinction imaging
Can I tune model for measured liquid penetration?
  No. Need more clarification about what is measured and modeled
What should I tune, plume direction or plume cone angle?
  Less plume direction, more plume cone angle
  Coupled, or one-way simulations have not shown superiority over simple cone-angle tuning to date
Can RANS or other simulation findings assist other more expensive models?
  Not yet. Plume cone seems to mean a completely different thing for each implementation

## Slide 35: END

## Slide 36: Analysis of #29 radiography
Also showing 34 degree plume direction
Notes: C:\pickett\ECN\mtgs\ECN5\topics\T9sprayGevap\scripts\radiography29.m