## Slide 1: ECN 7: flame structure TOPIC
Leonardo Pachano
CMT-Motores Térmicos
25th June 2020
Valencia, Spain

## Slide 2: Contributors
Qiyan Zhou, Tommaso Lucchini, POLIMI
Hesheng Bao, Bart Somers, TU/e
Fabien Tagliante, Noud Maes, Hyung sub, Julien Manin, Lyle Pickett, SNL
Emma Zhao, Muhsin Ameen, ANL
Wai Tong Chung, M. Ihme, SU
Leonardo Pachano, Daiana De Leon, José M Pastor, José M García,CMT

## Slide 3: Outline
Introduction
Summary of contributions
Inert mixing field
Assessment of modeling approaches
Transition from Spray A towards Spray D and Spray C
Summary
Future directions

## Slide 4: INTRODUCTION
Previous ECN workshops have focused on Spray A nozzle results:
  Detailed analysis on flame structure through different stages
  Comparison of model predictions with / LIF and high speed OH*
Spray Spray D and Spray C have received little attention so far:
  ECN 4/5: Experimental results ID/LOL/Penetration
  No contributions at ECN 6
No modeling contribution so far!
Background
Spray A at ECN 5

## Slide 5: INTRODUCTION
MOTIVATION
  Study of bigger nozzles representative of heavy-duty applications
    Nozzle size transition from Spray A towards Spray C/D
OBJECTIVES
  Assess sub-grid flame structure assumption and turbulence modeling approaches
  Evaluate changes in flame structure: Spray A towards Spray C/D
    Experiments and modeling approaches spatially-resolved
As from the guidelines

## Slide 6: Outline
Introduction
Summary of contributions
Inert mixing field
Assessment of modeling approaches
Transition from Spray A towards Spray D and Spray C
Summary
Future directions

## Slide 7: contributions
 | SNL | CMT
Nozzle | SA#A-3 [1] SD#209134 [2-3] SC#210037 [2-3] | SD#209135 [4]
Techniques | Schlieren imaging Formaldehyde and PAH imaging OH* chemiluminescence | OH* chemiluminescence
[1] ECN 6.12 https://ecn.sandia.gov/workshop/ECN7/ECN6.12.mp4
[2] ECN 6.14 https://ecn.sandia.gov/workshop/ECN7/ECN6.14.mp4
[3] https://doi.org/10.1016/j.applthermaleng.2020.115136
[4] https://doi.org/10.4271/2018-01-178
Experimental
Numerical
 |  | Yao |  |  | LLNL-hybrid |  | LLNL-detailed |  | Frassoldati |  | 
RANS | WM | ANL CMT POLIMI LLNL | ANL CMT POLIMI LLNL | ANL POLIMI | CMT | LLNL | LLNL | LLNL | POLIMI | POLIMI | POLIMI
 | Flamelet | CMT POLIMI | CMT POLIMI | POLIMI | CMT | CMT | - | - | POLIMI | POLIMI | POLIMI
LES | WM | - | - | - | SNL | SNL | - | - | - | - | -
 | Flamelet | TUe | - | - | - | - | - | - | - | - | -
 |  | SA | SD | SC | SA | SD | SA | SD | SA | SD | SC

## Slide 8: Computational setup
Numerical setup | ANL | CMT | POLIMI | SNL | SU | TUe
Nozzle | SA#210677 SD#209134 SC#210037 | SA#210675 SD#209135 - | SA#210675 SD#209134 SC#210037 | SA#A3 SD#209134 - | - SD#209134 - | SA#210677 - -
CFD code | CONVERGE v2.4 | CONVERGE v2.4 | OpenFoam | CONVERGE v3.0 | CharlesX | OpenFoam v2.4.x
Computational domain | CV vessel | CP vessel | CV vessel | CV vessel | CP BC at outlet | CV vessel
Grid type | AMR & fixed | AMR & fixed | Fixed | AMR & fixed | Structured-hexahed. | Fixed
Base grid [mm] | 4 | 2 | Spray-oriented, graded mesh | 2 | R = 20, X = 80 | Radial expansion 1.015 Radial expansion 1.01
Minimum cell size [mm] | 0.250 | 0.125 (SA) 0.250 (SD) | 0.2 | 0.0625 | 0.008 | 0.0625
Chemical mechanism | Yao - | Yao LLNL-hybrid | Yao Frassoldati | - LLNL-hybrid | Yao with 21 QSS species | Yao -
Combustion | WM - | WM UFPV | TWM TFPV | WM - | Finite-rate thickened-flame | - FGM
Turbulence | Standard | Standard | Standard | LES Dynamic Structure | LES + Vreman SGS | LES Dynamic Structure
Spray model | Lagrangian parcel | Lagrangian parcel | Lagrangian parcel | Lagrangian parcel | Real-fluids with Peng-Robinson EoS | Lagrangian parcel
Injection distribution | BLOB | Evenly distributed cone | Rosin-Ramler | BLOB | N/A | Rosin-Ramler
Breakup model | KH-RT w/o breakup length | KH-RT w/o breakup length | Reitz-Diwakar | KH-RT | N/A | KH-RT
Evaporation | Frossling | Frossling | StandardEvap | Frössling + Nguyen | N/A | liquidEvaporationBoil
Droplet collision | NTC | NTC | None | NTC | N/A | O’Rourke
Droplet drag | Dynamic sphere | Dynamic sphere | StandardGrag | Dynamic sphere + Nguyen | N/A | Sphere drag force
Droplet dispersion | O’Rourke | O’Rourke | GradientDisper | O’Rourke | N/A | Tsang
Numerical setup | ANL | CMT | POLIMI | SNL | SU | TUe
Nozzle | SA#210677 SD#209134 SC#210037 | SA#210675 SD#209135 - | SA#210675 SD#209134 SC#210037 | SA#A3 SD#209134 - | - SD#209134 - | SA#210677 - -
CFD code | CONVERGE v2.4 | CONVERGE v2.4 | OpenFoam | CONVERGE v3.0 | CharlesX | OpenFoam v2.4.x
Computational domain | CV vessel | CP vessel | CV vessel | CV vessel | CP BC at outlet | CV vessel
Grid type | AMR & fixed | AMR & fixed | Fixed | AMR & fixed | Structured-hexahed. | Fixed
Base grid [mm] | 4 | 2 | Spray-oriented, graded mesh | 2 | R = 20, X = 80 | Radial expansion 1.015 Radial expansion 1.01
Minimum cell size [mm] | 0.250 | 0.125 (SA) 0.250 (SD) | 0.2 | 0.0625 | 0.008 | 0.0625
Chemical mechanism | Yao - | Yao LLNL-hybrid | Yao Frassoldati | - LLNL-hybrid | Yao with 21 QSS species | Yao -
Combustion | WM - | WM UFPV | TWM TFPV | WM - | Finite-rate thickened-flame | - FGM
Turbulence |  |  |  | LES Dynamic Structure | LES + Vreman SGS | LES Dynamic Structure
Spray model | Lagrangian parcel | Lagrangian parcel | Lagrangian parcel | Lagrangian parcel | Real-fluids with Peng-Robinson EoS | Lagrangian parcel
Injection distribution | BLOB | Evenly distributed cone | Rosin-Ramler | BLOB | N/A | Rosin-Ramler
Breakup model | KH-RT w/o breakup length | KH-RT w/o breakup length | Reitz-Diwakar | KH-RT | N/A | KH-RT
Evaporation | Frossling | Frossling | StandardEvap | Frössling + Nguyen | N/A | liquidEvaporationBoil
Droplet collision | NTC | NTC | None | NTC | N/A | O’Rourke
Droplet drag | Dynamic sphere | Dynamic sphere | StandardGrag | Dynamic sphere + Nguyen | N/A | Sphere drag force
Droplet dispersion | O’Rourke | O’Rourke | GradientDisper | O’Rourke | N/A | Tsang

## Slide 9: contributions
Nozzle geometry | SA#675 | SA#677 | SA#A-3 | SD#134 | SD#135 | SC#037
Exit diameter [] | 89.4 | 83.7 | 94 | 191 | 190 | 208
Equivalent diameter [] | 489.46 | 458.26 | 517.27 | 1056.54 | 1045.54 | 989.97
Nozzle geometry | SA#675 | SA#677 | SA#A-3 | SD#134 | SD#135 | SC#037
 | 89.4 | 83.7 | 94 | 191 | 190 | 208
 | 489.46 | 458.26 | 517.27 | 1056.54 | 1045.54 | 989.97
Target condition
Parameter | Value
Fuel injection pressure [] | 150
Fuel Temperature [] | 363
Ambient gas density [] | 22.8
Ambient gas temperature [] | 900
Ambient gas composition | 15% , 75.15% 6.22% , 3.62%
Parameter | Value
 | 150
 | 363
 | 22.8
 | 900
Ambient gas composition | 
Nozzle geometry
[1] F.P. Ricou , D.B. Spalding , Measurements of entrainment by axisymmetrical tur- bulent jets, J. Fluid Mech. 11 (1) (1961) 21
[1]

## Slide 10: Outline
Introduction
Summary of contributions
Inert mixing field
Assessment of modeling approaches
Transition from Spray A towards Spray D and Spray C
Summary
Future directions

## Slide 11: INERT Mixing field
Do we all start from the same mixing state?
  Some variability around ideal adiabatic mixing
  Points at T > 900
Ideal adiabatic mixing
Reacting case at 0.1

## Slide 12: INERT Mixing field
Spray A
  Agreement with measurement in the far-field
Spray D
  Narrower radial profiles compared to measurements
Spray C
  Both modeling results match in the far-field
Adapted from ECN 7 https://ecn.sandia.gov/workshop/ECN7/ECN7.0.2.mp4
SNL LES  reacting case quasi-steady at x < LOL
SNL LES
Spray D

## Slide 13: Outline
Introduction
Summary of contributions
Inert mixing field
Assessment of modeling approaches
  RANS sub-grid flame structure assumption
  Turbulence model
Transition from Spray A towards Spray D and Spray C
Summary
Future directions

## Slide 14: Combustion Modeling approach
Lift-off length: Assessment of sub-grid flame assumption
Baseline setup  Spray D – YAO – RANS
Sub-grid flame assumption
  Well-mixed: ANL, CMT, LLNL, POLIMI*(TWM)
  Flamelet-based: CMT, POLIMI
In general:
LLNLWM #135
TWM
ANL WM #134
WM
POLIMI TWM #134
CMT WM #135
Flamelet
CMT UFPV #135
POLIMI TFPV #134
Exp. SNL #134
Exp. CMT #135
Definition based on

## Slide 15: Combustion Modeling approach
Species distribution: Assessment of sub-grid flame assumption
In general
  at LOL vicinity in fuel-rich “cold” mixtures
  OH around
WM  TWM
  Narrower
WM  Flamelet-based
  Longer extension
  Broader OH
False color images
CFD
Exp.
WM
Flamelet

## Slide 16: Outline
Introduction
Summary of contributions
Inert mixing field
Assessment of modeling approaches
  RANS sub-grid flame structure assumption
  Turbulence model
Transition from Spray A towards Spray D and Spray C
Summary
Future directions

## Slide 17: Comb. / Turbulence Modeling approach
Lift-off length
LLNLWM-RANS #135
Exp. SNL #134
Exp. CMT #135
SNL WM-LES #134
CMT WM-RANS #135
CMT UFPV-RANS #135
Baseline setup  Spray D – LLNL-h
  WM-LES: SNL
  WM-RANS: CMT, LLNL
  UFPV-RANS: CMT
WM-LES
  Comparable to UFPV-RANS
and yield similar results
WM-RANS
Definition based on
Markers  Definition based on
Experiments
ECN 6.13 Evaluation of hybrid LLNL 65 species mechanism including formaldehyde and OH*, and lift-off length definition

## Slide 18: Comb. / Turbulence Modeling approach
Species distribution
CFD OH-based
CFD OH*-based
Exp
Similar species distributions
  Wider for WM-LES and UFPV-RANS compared to WM-RANS

## Slide 19: Outline
Introduction
Summary of contributions
Inert mixing field
Assessment of modeling approaches
Transition from Spray A towards Spray D and Spray C
Summary
Future directions

## Slide 20: Transition SA  SD/SC
Exp. CMT #675
Exp. SNL #677
Exp. CMT #135
Exp. SNL #134
Exp. SNL #037
WM  longest LOL
  SA / SD
TWM  shortest LOL
Flamelet  differences among contributions
Consistent differences between predictions from SA to SD
Lift-off length

## Slide 21: Transition SA  SD/SC
Species distribution: WM
PAH
For most CFD results extends from spray radius towards the axis
Spray A RANS-WM with peak upstream LOL
Peak values for Spray D seems to be downstream from experimental observation

## Slide 22: Transition SA  SD/SC
Species distribution: Flamelet-based
High concentrations also seems to extend from the spray radius
Peak values seems to be downstream from experimental observation
PAH

## Slide 23: Transition SA  SD/SC
Exp. SNL #677
Exp. CMT #135
Exp. CMT #675
Exp. SNL #134
Exp. SNL #037
Mixture fraction at LOL
From SA  SD:
From SDSC:
  Subtle differences

## Slide 24: Outline
Introduction
Summary of contributions
Inert mixing field
Assessment of modeling approaches
Transition from Spray A towards Spray D and Spray C
Summary
Future directions

## Slide 25: Summary
Lift-off length location
  WM-RANS tends to the longest value  shorter value for WM-LES
  TWM-RANS tends to the shortest value  tabulation seems to have an important effect
  Flamelet-RANS lay in between  more reasonable compared to experiments
Species location
  Consistency among modeling approaches in the location of and
  WM-RANS show narrower regions compared to WM-LES and Flamelet-based
Modeling approaches

## Slide 26: Summary
Lift-off length location
  Both experiments and modeling results point at
  Predicted local mixing conditions at LOL
    from Spray A to Spray D / Spray C
    No clear trend from Spray D to Spray C
Species location
Nozzle transition
  Good agreement for SA
  Room for improvement for SD
    Maximum location
    LOL sensitivity to pre-burn?
      Exp. #134 pre-burn
      Exp. #135 /

## Slide 27: Outline
Introduction
Summary of contributions
Inert mixing field
Assessment of modeling approaches
Transition from Spray A towards Spray D and Spray C
Summary
Future directions

## Slide 28: Future directions
To analyze amount of produced
To include PAH in the flame structure analysis
To extend the analysis to other operating conditions
  Ambient temperature and sweep
  Local mixture conditions at LOL
  Possible liquid / flame interaction at higher-temperature conditions for Spray D and Spray C
Source: Maes et al., Applied Thermal Eng. 2020

## Slide 29: Future directions
Standardization of files to be shared / sharing method
Mixing predictability
For the comparison with PLIF results, the use of instead of from CFD might be more reasonable
Open topics
Spray A
Spray D
WM
Flamelet

## Slide 30: ACKNOWLEDGEMENTS
CMT-Motores Térmicos greatly acknowledge the financial support the Government of Spain through the CHEST Project (TRA2017-89139-C2-1-R).
Support for the Work conducted at the Combustion Research Facility, Sandia National Laboratories, Livermore, CA, was provided by the U.S. Department of Energy, Office of Vehicle Technologies and by Sandia National Laboratories under the Laboratory-Directed Research and Development (LDRD) program. Sandia National Laboratories is a multi-mission laboratory managed and operated by National Technology and Engineering Solutions of Sandia, LLC., a wholly ownedsubsidiary of Honeywell International, Inc., for the U.S. Department of Energy’s National Nuclear Security Administration under contract DE-NA0003525
Hesheng Bao from TU/e greatly acknowledge the financial support from China Scholarship council