## Slide 1
Hesham GABALLA, Chaouki HABCHI, Jean-Charles DE HEMPTINNE
IFP Energies Nouvelles
ECN 8.7 2/02/2023
Modeling and LES of high-pressure liquid injection under evaporating and non-evaporating conditions by a real-fluid model and surface density approach

## Slide 2: AGENDA
Introduction
Methodology
Results
Conclusions and perspectives

## Slide 3: Introduction
Chehroudi et al., 2012
Liquid injected into gaseous
(Single component system)
subcritical Pr=0.92
Transcritical Pr=1.22
Supercritical Pr=2.71
The injected fuel undergoes a continuous change of state from classical two-phase atomization to dense fluid mixing phenomenon.
Predictive CFD model for the fuel injection simulation under various thermodynamic regimes is required.
Spray modeling approaches
  Eulerian –Lagrangian approach Discrete Droplet Model (DDM),requires parameter tuning and not suitable for the dense near nozzle region.
  Eulerian-Eulerian approach
    Interface Capturing Methods (ICM) computationally expensive for industrial cases.
    Diffuse interface model (DIM),unresolved interface features are modeled instead of being tracked using a surface density approach.

## Slide 4: AGENDA
Introduction
Methodology
Results
Conclusions and perspectives

## Slide 5: Methodology
Real-fluid model (RFM) description
1-Governing equations (CONVERGE CFD solver)
2- Tabulated thermodynamic closure
Real-fluid EoS and Vapor-liquid equilibrium (VLE) calculations to consider phase change.
VLE coupled with real-fluid EoSs such as (PR, CPA, etc) is computed by in-house Carnot thermodynamic library before the CFD simulation and tabulated.
The tabulated quantities include:
  Thermodynamic & transport properties.
  Phase state & composition.

## Slide 6: Fuel Atomization (Surface density approach)
LES postulated model [3]
Coupled with the RFM
(Duret et al. 2013)
(Production/destruction term)
are provided by the RFM thermodynamic table as function of
Phase change effect on the surface density is implicitly considered by dependent on .
the liquid-gas interfacial area per unit volume.
[3] Chesnel et al. 2011,
(Anez et al, 2018)
Notes: *the minimum surface density that can be found for a given value of the resolved liquid volume fraction
*The first term on the RHS represents the turbulent diffusion flux modeled using a gradient law closure,
* The 2nd term on RHS represents the surface production/ destruction, due to turbulent flow stretching
and coalescence effects, which is modeled in a restoration to equilibrium form, where (S_eq)
is an equilibrium surface area density that should be reached within a characteristic time scale (taw).

## Slide 7: AGENDA
Introduction
Methodology
Results
Conclusions and perspectives

## Slide 8: Results
ECN spray A:
Fuel: n-dodecane ( C12H26)
Ambient composition: 100% N2
 | (1) Evaporating/Nominal | (2) Non-evaporating
(MPa) | 150 | 150
(K) | 900 | 303
(MPa) | 6 | 2
(kg/m3) | 22.8 | 22.8
(K) | 363 | 343
 | (1) Evaporating/Nominal | (2) Non-evaporating
 | 150 | 150
 | 900 | 303
 | 6 | 2
 | 22.8 | 22.8
 | 363 | 343
Case study for model validation

## Slide 9: Results
ECN spray A:
Fuel: n-dodecane ( C12H26)
Ambient composition: 100% N2
 | (1) Evaporating/Nominal | (2) Non-evaporating
(MPa) | 150 | 150
(K) | 900 | 303
(MPa) | 6 | 2
(kg/m3) | 22.8 | 22.8
(K) | 363 | 343
 | (1) Evaporating/Nominal | (2) Non-evaporating
 | 150 | 150
 | 900 | 303
 | 6 | 2
 | 22.8 | 22.8
 | 363 | 343
(2) non-evaporating case: ECN X-ray measurements for spray dispersion.
ECN Ultra small angle X-ray scattering (USAXS) measurements for interfacial area and SMD.
Case study for model validation

## Slide 10: AGENDA
Introduction
Methodology
Results
  Non-evaporating spray A
  Nominal evaporating spray A
Conclusions and perspectives

## Slide 11: Spray A setup
Base Grid
Base size:
Min size:
Cell count G1 (3M), G2 (16M), G3 (21M)
15 cells on the orifice (D=0.089mm-serial #21067 )
Inlet
Nozzle exit
Lx=20mm, Ly=Lz=10mm
CONVERGE V3.0.15 - RFM
Thermodynamic table: VTPR EoS for C12/N2 binary system.
PISO algorithm
Spatial scheme: 2nd order central.
Temporal scheme: Semi implicit Crank- Nicolson scheme
Turbulence modeling: LES Sigma model
2-3ns, CFL controlled with max
Time varying inlet mass flow rate profile (CMT)[4]
Fluctuating Inflow BC (Fourier method)
  I=3% [5] , length scale= 2
[4] CMT. https://www.cmt.upv.es/ECN03.aspx
[5] Desantes et al. (2017, 2020)

## Slide 12: Fuel projected mass density (PMD)
r
LES time avg
EXP
Time- averaged LES- Grid 2
ECN X-ray data[6]
PMD: line of sight integration of fuel density along spray depth
Quasi-steady period
[6]ECN X-ray radiography, https://ecn.sandia.gov/rad675.

## Slide 13: FUEL Dispersion (Projected mass density)
r
Grids
Grid 1 cells
Grid 2 cells
Grid 3 cells
Model results are in good agreement with the experimental data, especially using G2 and G3.

## Slide 14: FUEL Dispersion (Projected mass density)
r
Grids
Grid 1 cells
Grid 2 cells
Grid 3 cells
Model results are in good agreement with the experimental data, especially using G2 and G3.
G2 is used for further calculations .

## Slide 15: FUEL Dispersion (TIM and LVF)
Transverse integrated mass (TIM)

## Slide 16: FUEL Dispersion (TIM and LVF)
Transverse integrated mass (TIM)
TIM is well captured until 5mm, then tends to be overestimated.
LVF is matched with great accuracy reproducing intact liquid core and decay along spray centerline.

## Slide 17: Atomization model assessment
Ultra small angle X-ray scattering (USAXS) experiments [7]: projected surface area density along the spray centerline.
2 model constants ()
Projected surface area density is well reproduced along the spray axis.
SMD falls within the experimental data range.
[8]: Kastengren et al. (2017)
[9]: Desantes et al. (2017,2020)
[10]: Demoulin el al., (2013)

## Slide 18: AGENDA
Topic & objectives
Methodology
Description of simulated test case
Results
  Non-evaporating spray A
  Nominal evaporating spray A
Conclusions and perspectives

## Slide 19: Results
ECN spray A:
Fuel: n-dodecane ( C12H26)
Ambient composition: 100% N2
 | (1) Evaporating/Nominal | (2) Non-evaporating
(MPa) | 150 | 150
(K) | 900 | 303
(MPa) | 6 | 2
(kg/m3) | 22.8 | 22.8
(K) | 363 | 343
 | (1) Evaporating/Nominal | (2) Non-evaporating
 | 150 | 150
 | 900 | 303
 | 6 | 2
 | 22.8 | 22.8
 | 363 | 343

## Slide 20: Spray A- evaporating condition
GRID: 16M cells
Inlet mass flow profile (CMT)
without a Fluctuating inflow BC
Liquid pen: LVF=0.15%
Vapor pen: Yc12=0.1%
The Liquid and vapor penetrations match well with the Experiments

## Slide 21: Spray A- evaporating condition
GRID: 16M cells
Inlet mass flow profile (CMT)
without a Fluctuating inflow BC
Liquid pen: LVF=0.15%
Vapor pen: Yc12=0.1%
Fuel radial distribution fairly agrees with the Exp.

## Slide 22: Droplet SMD- evaporating vs Non-evaporating case
Droplet size reduces under the evaporating condition.
The result show the sensitivity of the surface density model to the phase change, which is automatically provided by the RFM model.

## Slide 23: AGENDA
Topic & objectives
Methodology
Description of simulated test case
Results
  Non-evaporating spray A
  Nominal evaporating spray A
Conclusions and perspectives

## Slide 24: CONCLUSIONS & Perspectives
Conclusions
  RFM model coupled with a SGS atomization model based on a surface density approach for atomization modeling within LES framework.
  Fuel dispersion & atomization are well predicted using (RFM-LES) (non-evaporating Spray A).
  Under (evaporating Spray A) condition, the spray penetrations and fuel distribution are well predicted.
Perspectives
  Investigation of renewable fuels injection such as (Methanol/ammonia) under the Spray A condition.
  Including the in-nozzle flow in the simulation (especially for cavitating injectors)

## Slide 25: acknowledgments
This project has received funding from the European Union Horizon 2020 Research and Innovation programme. Grant Agreement No 861002 for the EDEM project.

## Slide 26: Thank you for your attention QUESTIONS ?