## Slide 1: ECN9 – diesel-like AMMONIA SPRAYS
José M García-Oliver
ECN 9 Workshop | Naples, Italy on September 8th – 9th, 2023

## Slide 2: ECN9 – diesel-like AMMONIA SPRAYS
INERT
  Gabriela Bracho, Jiawei Cao
REACTING
  Andrea Schirru, Tommaso Lucchini
  Andrea Di Matteo, Bart Somers
CONTRIBUTORS

## Slide 3: ECN9 – diesel-like AMMONIA SPRAYS
This research has been partially funded by MCIN/AEI/10.13039/501100011033 and the European Union “NextGenerationEU”/PRTR as part of the projects TED2021-129379A-I00 and SAFLOW TED2021-131618CA-C22
We would like to thank José Enrique del Rey and Omar Huerta for their valuable support during the experimental campaign at CMT
Thanks to Kar Mung Pang from MAN Energy Solutions for fruitful discussion
ACKNOWLEDGEMENTS

## Slide 4: MOTIVATION
Operating conditions
Reference Nozzles
  Spray M, single-hole & multi-hole
  Spray G, multi-hole
  Bosch 7-hole
  Spray D, Single-hole
Fuels
  Ammonia
GUIDELINES – WISH LIST ?
Injector type | Name | T fuel [K] | P fuel [bar] | T amb [K] | P amb [bar] | rho amb [kg/m3] | O2 [%] | Injection duration [ms]
M (1,8), G, Bosch7 | Ambient fuel | 293 | 120, 200 | 293 | 0.5, 2, 15 | varies | 0 | > 3
 | Hot fuel | 363 | 200 | 333 | 0.5, 60 | varies | 0 | > 3
 | Hot fuel & air | 363 | 200 | 573 | 6 | 3.5 | 0 | > 3
D | Diesel-like | 363 | 1500 | 1200, 1300 | varies | 22.8 | 0, 21 | > 3

## Slide 5: MOTIVATION
Most of the groups are facing difficulties to operate Diesel-like injectors with ammonia
Modelling efforts have been only achieved by groups with traditional activity within ECN
… REALITY
The menu is served
  Inert spray: Exp-only by CMT
  Reacting sprays: CFD-only by TUe + Polimi

## Slide 6: Diesel like ammonia sprays inert

## Slide 7: Inert ammonia sprays
Approach
Materials and methods
  Experimental facility
  Optical setup
  Test Conditions
Results and discussion
  Spray penetration and spray angle
  Effect of chamber conditions and injection pressure
THE CONTENTS

## Slide 8: Inert ammonia sprays
This presentation will present a first characterization of ammonia sprays under a Diesel-like configuration using ECN recommendations [1] … except for the injector!!
  Vapor phase penetration and cone angle vs time: single-pass Schlieren
  Liquid length: diffuse back illumination (DBI)
Parametric study:
  Ambient gas density, ambient gas temperature
  Rail pressure conditions
[1] García-Oliver JM, Bracho G, de la Morena J, Cao J, 2nd Symposium on Ammonia Energy, 2023
APPROACH

## Slide 9: Materials and Methods
Experimental Facility: High Pressure High Temperature Test rig
  Continuous flow operation
  Wide range of operating conditions:
    Gas: [N2] or [N2+O2]
    Temperature up to 1100K
    Pressure: up to 150 bar
  Wide testing section: Ø200mm
  Injector holder with a cooling adaptor
Nozzle
9

## Slide 10: Materials and Methods
Experimental facility: Common Rail Injection system description
  Liquid ammonia was supplied from a storage tank  NH3 Cooled down to prevent cavitation in the pump
  A pneumatic pump was used
  To prevent phase change in the injector:
    Return-leakage line was pressurized [10 bar]
    Adjustable injector cooling temperature [15ºC]
  All the return lines were collected  acid trap
15-18 bar
Heating blankets
[50ºC]
10
The system operated in stabilized conditions up to Pinj 800 bar
Notes: Around 40ºC in storage

## Slide 11: Materials and Methods
Test Conditions:
Gas Temp. [K] | Pinj [bar] | Oxygen [%] | Density [kg/m3]
800 900 | 600 800 | 0 | 22.8 30.4
Nozzle | Diameter | 
Solenoid – Bosch | 300 µm | 
- Single hole nozzle, convergent
Bosch Spray D-like Injector
Injection frequency: every 4 sec.
Energizing Time: 2 ms -> Injection duration 3 ms
Sample size: 20 injection cycles
11

## Slide 12: Materials and Methods
Optical setup:
  Vapor phase penetration: Conventional single-pass Schlieren
    Image size: 768x272 pix
    Spatial resolution: 4.2 pix/mm
    Image acquisition: 60 kfps
    Exposure time: 0.6 µs
Parabolic mirror
Light source
Lens
Iris
12

## Slide 13: Materials and Methods
Optical setup:
  Liquid length: Diffuse Back Illumination (DBI)
    Image size: 768x272 pix
    Spatial resolution: 4.2 pix/mm
    Image acquisition: 60 kfps
    Exposure time: 15 µs
    LED @ 660nm
LED
Diffuser
Lens
13

## Slide 14: Materials and methods
EXAMPLE OF RAW IMAGES
14
T=900 K – rho=22.8 kg/m3 – Pinj = 600 bar

## Slide 15: Results
NH3 Overall behaviour similar to Diesel BUT
  Initial phase of the injection is slower in the NH3 spray
  Stabilized LL of NH3 is shorter
Open points
  Different density, lower viscosity
  Internal nozzle flow and dynamic operation of the injector?
  Needle lift? Actual injection rate differences?
COMPARISON WITH CONVENTIONAL DIESEL
Injection Pressure: 600 bar
15
Notes: La densidad es 22.8

## Slide 16
SPRAY ANGLE EVOLUTION
NH3
Diesel
Injection Pressure: 600 bar
S
Angle criteria: Angle fitted between 10% - 60% spray region
Wider spray angle for NH3 at the start of injection  later behaviour is pretty similar
16
Results
COMPARISON WITH CONVENTIONAL DIESEL
Notes: La densidad es 22.8

## Slide 17
Effect of injection rail pressure
  Gas density: 22.8 kg/m3
  Temp 800K
LIQUID PHASE
VAPOR PHASE
17
Results
PARAMETRIC VARIATIONS
Mixing-controlled LL

## Slide 18
Effect of chamber temperature
  Gas density: 22.8 kg/m3
  Injection pressure 800 bar
18
Results
PARAMETRIC VARIATIONS
LIQUID PHASE
VAPOR PHASE
Notes: Añadir barras de error

## Slide 19
Effect of chamber density
  Gas Temperature: 900K
  Injection pressure 800 bar
19
Results
PARAMETRIC VARIATIONS
LIQUID PHASE
VAPOR PHASE
Notes: Añadir barras de error

## Slide 20: Conclusions – inert
Inert ammonia sprays were investigated for a 300µm nozzle
A common-rail type system has been employed. Needed adaptations:
  Return-leakage line was pressurized [10 bar]
  Adjustable injector cooling temperature [15ºC]
Spray penetration results showed significant differences between NH3 and conventional diesel during the initial transient phase of the process
  Later evolution becomes similar to that of Diesel
Trends in parametric variationssimilar behaviour as Diesel sprays
  Injection pressure, ambient temperature, density variations hint at mixing-controlled, gas-jet behaviour
20

## Slide 21: Diesel like ammonia sprays reacting

## Slide 22: reacting AMMONIA SPRAYS
Introduction & Motivation
Numerical setup
  Domain/Mesh
  Turbulence model
  Spray
  Combustion
Spray mixing characteristics
Combustion results
  ID/Tmax
  Flame stabilization
Combustion – Flamelet behaviour
CONTENTS

## Slide 23: INTRODUCTION
PROPOSED EXPLORATORY STUDY
  Numerical analysis (‘blind experiment’) of ammonia spray combustion under diesel-like environment
  Evaluation of potential future research within ECN
FOCUS OF ANALYSIS
  Ammonia ignition sequence / potential
  NOx formation
ECN CONTEXT

## Slide 24: introduction
Idea ‘borrowed’ from presentation by Bakir et al [1]
AS OF GUIDELINES
[1] Bakir, A. H., Ge, H., Zhang, Z., & Zhao, P. (2023). International Journal of Engine Research, 146808742311773. https://doi.org/10.1177/14680874231177361

## Slide 25: introduction
Idea ‘borrowed’ from presentation by Bakir et al [1]
AS OF GUIDELINES
[1] Bakir, A. H., Ge, H., Zhang, Z., & Zhao, P. (2023). International Journal of Engine Research, 146808742311773. https://doi.org/10.1177/14680874231177361

## Slide 26: MOTIVATION
Operating conditions
Reference Nozzles
  Spray M, single-hole & multi-hole
  Spray G, multi-hole
  Bosch 7-hole
  Spray D, Single-hole
Fuels
  Ammonia
GUIDELINES – WISH LIST
Injector type | Name | T fuel [K] | P fuel [bar] | T amb [K] | P amb [bar] | rho amb [kg/m3] | O2 [%] | Injection duration [ms]
M (1,8), G, Bosch7 | Ambient fuel | 293 | 120, 200 | 293 | 0.5, 2, 15 | varies | 0 | > 3
 | Hot fuel | 363 | 200 | 333 | 0.5, 60 | varies | 0 | > 3
 | Hot fuel & air | 363 | 200 | 573 | 6 | 3.5 | 0 | > 3
D | Diesel-like | 363 | 1500 | 1200, 1300 | varies | 22.8 | 0, 21 | > 3
  Ref chemical mechanism: Otomo et al. Int J Hydrogen Energy 2018; 43: 3004–3014 32 species / 211 reactions

## Slide 27: COMPUTATIONAL SETUP
MESH | TU/e | PoliMi
Type | 3D Cylindrical | 2D Wedge
# Cells | 2.85 M | 50 K
Min. Cell Size | 200 μm | 400 μm
Length | 0.24 m | 0.5 m
Radius | 35 mm | 100 mm
SPRAY Reitz KHRT | TU/e (Modified) | PoliMi
B0 | 0.1 | 0.61
B1 | 40 | 40
Ctau | 1 | 1
CRT | 0.1 | 0.1
Cone Angle | 19° | 14°
For PoliMi the standard evaporation model of OpenFOAM was used. A modified version is used for TU/e
ROSIN-RAMLER | TU/e (RR) | PoliMi (uniform)
min | 30 μm | 186 μm
max | 186 μm | 186 μm
SMD | 50 μm | 186 μm

## Slide 28: COMPUTATIONAL SETUP
k - ε | TU/e (RR) | PoliMi (uniform)
C1 | 1.59 | 1.55
Cmu | 0.09 | 0.09
C2 | 1.92 | 1.92
C3 | -0.33 | 0
Sigma k | 1 | 1
Sigma ε | 1.3 | 1.3
TCI models
  TUe:
    FGM: Tabulation, progress variable in terms of species
  PoliMi
    DETAILED KINETICS: Well-mixed with dynamic load balancing
    TRIF: Tabulation, progress variable in terms of enthalpy

## Slide 29: Overall mixing comparison
PENETRATION + EVAPORATION
Slightly faster penetration in FGM

## Slide 30: OVERALL MIXING COMPARISON
AXIAL VELOCITY DISTRIBUTION BEFORE IGNITION
Slightly faster penetration in FGM -> Higher velocity

## Slide 31: Overall mixing comparison
MIXTURE FRACTION BEFORE IGNITION
Slightly faster penetration in FGM -> Slower mixing

## Slide 32: Overall mixing comparison
Differences among models in mixing behaviour due to
  Mesh
  Turbulence model (small)
  Not likely to spray calibration

## Slide 33: Ignition – 1200 K
Ignition after EOI, spray dilution
ID [ms] | D-K | TRIF | FGM
1200 K | 9.48 | 9.3 | 5.91
1300 K | 2.05 | 3.64 | 1.91
ID based upon Tair+400K

## Slide 34: Ignition – 1300 K
Ignition in a sustained spray
ID [ms] | D-K | TRIF | FGM
1200 K | 9.48 | 9.3 | 5.91
1300 K | 2.05 | 3.64 | 1.91
ID based upon Tair+400K

## Slide 35: IGNITION SEQUENCE
Temperature maps
FGM
TRIF
DK

## Slide 36: Ignition sequence
Side ignition– only captured for FGM due to saving discretization
FGM
TRIF
DK
Fuel age calculation for a n-heptane jet
0.002 s
Side ignition as a result of ‘oldest’ fuel?

## Slide 37: Flame stabilization
SUSTAINED FLAME?
FGM
TRIF
DK
Full reaction zone under lean conditions
  Peak temperature correlates with leanest mixtures
0.005 s
Lean

## Slide 38: Flamelet analysis
1200 K - Strain rate 50 1/s
Consistency with CFD spray results
  Late ignition
  Progress from lean towards rich
  Lean branch always on the steady flamelet

## Slide 39: Reacting penetration
Ignition amplifies inert differences

## Slide 40: CONCLUSIONS – reacting
First trials hint at
  Ignition at around end of injection (5 ms!!) for 1200K
  Igniting sprays before end of Injection at 1300 K
    Side ignition due to extreme low ignitability, role of fuel age
    Stabilized flame seems to occur?
  Higher temperatures could further decrease ID and lead to a very similar Diesel like combustion
Combustion always under lean conditions
  Combustion regime?
Vast need of experimental validation

## Slide 41: Future directions
Nozzle flow analysis
Injection rate measurements?
CFD Simulations
A LONGER WISH LIST?
41

## Slide 42: FUTURE DIRECTIONS
More reactive conditions
  Adding H2 in the ambient air, following the simulation work by Bakir et al that inspired the ECN9 proposal.
    Not feasible for constant-pressure vesseIs, more feasible in constant-volume ones with a second injector
  Using a pilot spray with a more reactive fuel: Recent work by the group at TU Munich by Scharl et al, Fuel 333 (2023) 126454
    Reference experiment with two injectors, at an angle to allow spray intersection
POTENTIAL PATHS FOR REFERENCE STUDIES

## Slide 43: Thank you, questions?

## Slide 44: Backup slides

## Slide 45: Materials and Methods
Data processing:
  The images have been processed following the procedure developed at CMT from previous works [1,2]*
[1] | R. Payri, J. M. García-Oliver, M. Bardi and J. Manin, “Fuel temperature influence on diesel sprays in inert and reacting conditions,” Applied Thermal Engineering, vol. 35, pp. 185-195, 2012.
[2] | R. Payri, F. Salvador, J. Gimeno and L. Zapata, “Diesel nozzle geometry influence on spray liquid-phase fuel penetration in evaporative conditions,” Fuel, vol. 87, pp. 1165-1176, 2008.
Steps:
Background Correction
Spray boundaries detection
Contour analysis
Penetration (S)
Liquid Spray Angle (θ)
NH3 Vapor phase
NH3 Liquid phase (LL)
Nozzle tip
Example of raw images
Example of contour detection
Nozzle tip
Nozzle tip
Nozzle tip
45

## Slide 46: CONCLUSIONS
Non-reacting sprays of ammonia were investigated to obtain the LL and vapor tip penetration at high injection pressure condition
A common-rail type system has been employed. To prevent phase change in the injector:
  Return-leakage line was pressurized [10 bar]
  Adjustable injector cooling temperature [15ºC]
Spray penetration results showed significant differences between NH3 and conventional diesel (used as reference), especially in the transient phase of the process.

## Slide 47: Computational setup
Numerical setup | POLIMI | TUe
CFD code | OpenFoam | OpenFoam v2.4.x
Computational domain | CV vessel | CV vessel
Grid type | Fixed | Fixed
Base grid [mm] | Spray-oriented, graded mesh | Radial expansion 1.015 Radial expansion 1.01
Minimum cell size [mm] | 0.2 | 0.0625
Chemical mechanism | Yao | Yao -
Combustion | TWM TFPV | FGM
Turbulence | Standard | LES Dynamic Structure
Spray model | Lagrangian parcel | Lagrangian parcel
Injection distribution | Rosin-Ramler | Rosin-Ramler
Breakup model | Reitz-Diwakar | KH-RT
Evaporation | StandardEvap | liquidEvaporationBoil
Droplet collision | None | O’Rourke
Droplet drag | StandardGrag | Sphere drag force
Droplet dispersion | GradientDisper | Tsang
Numerical setup | POLIMI | TUe
CFD code | OpenFoam | OpenFoam v2.4.x
Computational domain | CV vessel | CV vessel
Grid type | Fixed | Fixed
Base grid [mm] | Spray-oriented, graded mesh | Radial expansion 1.015 Radial expansion 1.01
Minimum cell size [mm] | 0.2 | 0.0625
Chemical mechanism | Yao | Yao -
Combustion | TWM TFPV | FGM
Turbulence |  | LES Dynamic Structure
Spray model | Lagrangian parcel | Lagrangian parcel
Injection distribution | Rosin-Ramler | Rosin-Ramler
Breakup model | Reitz-Diwakar | KH-RT
Evaporation | StandardEvap | liquidEvaporationBoil
Droplet collision | None | O’Rourke
Droplet drag | StandardGrag | Sphere drag force
Droplet dispersion | GradientDisper | Tsang