## Slide 1: ECN9 AMMONIA GUIDELINES
Topic LEADS
M Battistoni, UNIPG
J M García-Oliver, CMT
Presented: 1 June 2023
to participate, please contact us:
michele.battistoni@unipg.it
jgarciao@mot.upv.es

## Slide 2: CONTENTS
Overall Introduction
Ammonia topics
  Internal flow, near field, vaporization and mixing
  Combustion

## Slide 3: OVERALL INTRODUCTION
General guidelines
  From nozzle flow through vaporizing spray, combustion and emissions
  Improving synergy among groups working on ammonia as a fuel
Motivation
  Growing interest on zero-carbon fuel for transportation and power
  Availability of ammonia as chemical ammonia for power
Ammonia combustion can be achieved through
    High compression ratios
    Spark-ignition under near-stoichiometric/lean conditions
    Pilot-ignition under lean and very lean conditions
    Booster/enhancer, like H2 from reforming

## Slide 4: OVERALL INTRODUCTION
From ECN8:
  Spray D remains of interest for combustion systems based on diesel hardware
  Also spray G, operating up to 200 bar injection pressure for SI engines
Highlights for ECN9:
  New GDI type injector: spray M, capable of up to 350 bar injection pressure
    single-hole & 8-hole nozzles
  GDI Bosch 7-hole injector

## Slide 5: OVERALL INTRODUCTION
Operating conditions
Reference Nozzles
  Spray M, single-hole & multi-hole
  Spray G, multi-hole
  Bosch 7-hole
  Spray D, Single-hole
Fuels
  Ammonia
Injector type | Name | T fuel [K] | P fuel [bar] | T amb [K] | P amb [bar] | rho amb [kg/m3] | O2 [%] | Injection duration [ms]
M (1,8), G, Bosch7 | Ambient fuel | 293 | 70, 120, 200 | 293 | 0.5, 2, 15 | varies | 0 | > 3
 | Hot fuel | 363 | 200 | 333 | 0.5, 60 | varies | 0 | > 3
 | Hot fuel & air | 363 | 200 | 573 | 6 | 3.5 | 0 | > 3
D | Diesel-like | 363 | 1500 | 1200, 1300 | varies | 22.8 | 0, 21 | > 3

## Slide 6: CONTENTS
Overall Introduction
Ammonia topics
  Internal flow, near field, vaporization and mixing
  Combustion

## Slide 7: 1. Internal flow, near field, vaporization and mixing 1/2
OBJECTIVES
Study:
Internal flow and near-field dynamics: primary break-up, cone angle, flash boiling, and related flow features of single-hole vs. multi-hole
Parameters:
  Effect of ambient pressure
  Room temperature fuel vs. Heated fuel
  Intake-stroke injection vs. compression-stroke injection
  Effect of injection pressure
  Open questions:
  Does flash-boiling always occur? Does it start inside the orifice or externally?
  How much does jet collapse affect mixing behavior? (single vs. multi-hole)
  Are ammonia liquid properties affecting spray formation and mixing fields, in such a way that new predictive models are needed?
  Transcritical paths with ammonia: dense-fluid approach vs. break-up & evap.?
  What minimum temperature do we reach? Does it get compensated heating the fuel?

## Slide 8: 1. Internal flow, near field, vaporization and mixing 2/2
REQUESTED INFO (both Experiments and Simulations, where applicable)
  Mass & momentum flow rates
  Tip penetration, near nozzle cone angle vs. time
  Transverse integrated mass (TIM) vs. axial distance
  2D contours of liquid volume fraction (LVF) and on cross-sections for sim.
  2D contours of projected liquid density and projected liquid volume (PLV)
  Mean droplet size (SMD) and PDF of liquid drop diameters
  Liquid and vapor mass fractions (either as projected quantities or as cut-plane values for sim.)
  Temperature fields, both liquid and gas phase
  Velocity fields, both liquid and gas phase
  Mixing fields
  In addition: raw data from simulations in VTK format are accepted as well. Quantities of interest will be extracted and shared with the ECN (with permission of submitters). Please contact the organizers to discuss submission of VTK format files.

## Slide 9: CONTENTS
Overall Introduction
Ammonia topics
  Internal flow, near field, vaporization and mixing
  Combustion

## Slide 10: 2. COMBUSTION 1/2
PROPOSED EXPLORATORY STUDY
  Numerical analysis (‘blind experiment’) of ammonia spray combustion under diesel-like environment
  Evaluation of potential future research within ECN
FOCUS OF ANALYSIS
  Ammonia ignition sequence / potential
  NOx formation

## Slide 11: 2. COMBUSTION 2/2
CONDITIONS
  Spray D – Injection pressure 1500 bar
  Ambient density 22.8 kg/m3
  Ambient temperature 1200/1300 K
  Ambient oxygen 21%
  Chemical mechanism:
    Reference: Otomo J, Koshi M, Mitsumori T, Iwasaki H and Yamada K. Chemical kinetic modeling of ammonia oxidation with improved reaction mechanism for ammonia/air and ammonia/hydrogen/air combustion. Int J Hydrogen Energy 2018; 43: 3004–3014
    Other mechs are also welcome for comparison purposes (please contact organizers)
REQUESTED INFO
  Time-resolved tip penetration, Tmax, heat release rate
  Species and temperature fields

## Slide 12: CONCLUSION
Call for contributors!