## Slide 1: Hydrogen Injection (Noud Maes)
MOTIVATIONS
  Heavy-duty, off-road, & stationary applications are the main driver for hydrogen
  Better understanding of injection, mixture formation, and ignition of DI hydrogen injections
OBJECTIVES
  Understanding the different processes with what’s available, regardless of conditions/injectors
  Experiments and simulations looking at single free jets
  Experiments and simulations aiming at understanding ignition and flame stabilization
TARGET CONDITIONS
  0.65-mm single (straight)-hole modified Bosch HDEV 1.2 injector
  100 bar injection (293 K, 10 bar (nPR = 10), N2 (inert) ambient) * Aligning with TU/e & IFP .stp available
    Injection pressure variations: 80 bar & 40 bar (nPR = 8 & 4)
    Ambient pressure variation: 40 bar & 1 bar (nPR = 2.5 & nPR100)
    Temperature variation @ 21% O2 for simulations: 1200 K and 40 bar ambient pressure (nPR 2.5)

## Slide 2: Hydrogen Injection (Noud Maes)
INFORMATION OF INTEREST
  Available information for general overview of activities? In addition to “new”:
  Injection and mixing data
    Experiments: mass flow rate, momentum flow rate, spray penetration, time-resolved mixing fields
    Simulations: nozzle discharge/pressure increase chamber, spray penetration, time-resolved mixing-, temperature-, velocity-, and turbulence fields
  Ignition and flame stabilization and flame structure data
    Experiments: Ignition delay, time-resolved OH* (or OH LIF, CH*, etc.)
    Simulations: Ignition delay, time-resolved species maps (H2, OH, NO, H2O)