## Slide 1: ECN2 Future Direction
Continue
  Spray A baseline
  Soot
New
  Large, single-hole nozzle.
  Spray B
  GDI injector
  Transparent nozzle
  Engine flows
Address physical problems
  Internal flow/near nozzle
  Supercritical
  Turbulence/chemistry interaction at engine conditions

## Slide 2: ECN2 Future Direction
Continue
  Spray A baseline
  Soot
New
  Large, single-hole nozzle.
  Spray B
  GDI injector
  Transparent nozzle
  Engine flows
Address physical problems
  Internal flow/near nozzle
  Supercritical
  Turbulence/chemistry interaction at engine conditions
Carried out
Started
Coming soon

## Slide 3: ECN2 : Physical problem challenges
Understanding internal nozzle flow, nozzle geometry, and its connection to the near field spray
  Suggested hardware
    Spray B, transparent nozzle (large nozzle), sharp-edged axial single-hole nozzle
  Potential experiments
    Phase-contrast, radiography, high-res. x-ray tomography, transparent visualization, momentum and mass flow rate, near-field long-distance microscopy, L2FV, ballistic imaging
  Potential modeling projects
    Internal flow CFD with cavitation
    Effects of grid size and surface roughness and “imperfections”
    Primary atomization
    B.C.s that include nozzle gas in the sac and initial wall temperature distribution
    Hydraulic model of injector, (e.g. AMESIM)
Carried out
Started
Coming soon

## Slide 4: ECN2: Physical problem challenges
Is Spray A "supercritical"? (a dense fluid)
  Potential experiments
    long-distance microscopy high speed imaging, PDA near LL, Ballistic imaging, others (Raman spectroscopy?)
  Potential modeling projects
    models that treats dense fluid
    Develop a light model for photons interacting with dense fluids
Carried out
Started
Coming soon

## Slide 5: ECN2: Physical problem challenges
Turbulence/chemistry interaction at "engine type conditions"
  Hardware
    Multiple injections, wall impingement (liquid or vapor?), large nozzles, fuels, RCM
  Potential experiments
    OH/CH2O, PIV, transient lift off, chemiluminescence, schlieren, Temperature (Raman), LIF, Rayleigh, other species? (NO…)
  Potential modeling projects
    Chemistry mechanisms
    Continuation of model comparisons
    Modeling experimental measurements (OH LIF…)
Carried out
Started
Coming soon

## Slide 6
Topic 2: Recommendation for Simulations
EE models need a primary breakup model, since the turbulence mixing based models only capture mixing but not spray breakup
Simulations with high needle lifts need to reduce the initial lift values, otherwise they run the risk of completely missing the initial transients. At 20 μm min. lift, injection velocity is already quite high for Spray A
Is Spray A supercritical?
  Yes/No/Unsure
  What are the implications to modeling these sprays if they are indeed supercritical?
Simulations need to account of liquid compressibility and temperature variations
There is a clear evidence of the gas in the sac. Sub-merged nozzle flow simulations are not accurate
Need more Grid resolution!
2-D results are good and computationally cheap, needle off-axis motion and geometric asymmetries necessitate 3-D simulations

## Slide 7
Topic2: Recommendation for Experiments
Data not reliable in some cases due to injector coking issues. Some guidelines developed on how to handle the injectors under the reacting environments.
  ECN requirement is to measure flow rate before and after tests
  There are also other storage and handling requirements
Radial mixture fraction and velocity distributions were available beyond 20 mm. Possible to perform these measurements in the near nozzle region using optical techniques?
Simulations predict significant temperature drop as the fuel exits the nozzle. Density reconstruction at the nozzle exit possible?
Similar to Spray A: (1) quantification of differences between Spray B injectors, (2) Robust parametric variations

## Slide 8
Topic 2: ECN 4: Grand Challenge
Experiments and simulations to work together and identify means to transition from EE to LE models (since topic 1.3 and topic 2 were mostly LE)
This is not a new problem, researchers have attempted these transitions before, but the transitions seem rather empirical in nature and lose fidelity from the EE calculations
Perhaps long-distance microscopy and droplet size measurements can aid in the development of such models
IFPEN Calculation
Argonne X-ray experiments

## Slide 9: Topic 2: RECOMMENDATIONS FOR ECN3
SIMULATIONS
  A more accurate chemistry model is needed
      Subtopic for ECN4?
      Why not testing spray A with a fuel with a better known chemistry, e.g. n-heptane?
  Well-mixed model issue less accurate predictions of ID/LOL than TCI ones
  BUT more validation is needed to fully discern prediction capabilities regarding
      Velocity field (PIV), FL, Penetration

## Slide 10: Topic2: RECOMMENDATIONS FOR ECN3
SIMULATIONS
  Inert vs reacting spray
      Always simulate an inert case as a baseline upon which the reacting case can be compared
      This can rule out differences due to spray mixing
  Soot models need to be investigated with a closer look at the combustion model
  LES contributions are welcome
NOZZLE FLOW
NEAR NOZZLE
EVAPORATIVE SPRAY
COMBUSTION
SOOT

## Slide 11: Topic 2: RECOMMENDATIONS FOR ECN3
EXPERIMENTS
  Any technique that delivers information on local temperature/composition under reacting condition is welcome!
      More 2D Information is essential
  More extensive radiation measurements
      Closer look into soot-radiation link
ANALYSIS FROM EXPERIMENTS+MODELLING
  Are we able to describe the spray flow time evolution?

## Slide 12: Topic 2: RECOMMENDATIONS FOR ECN3
ADDITIONAL IDEAS
  After EOI flame dynamics
  DB extension with multiple injections/larger orifice size

## Slide 13: Topic 2: future directions?
Multiple injections
  Spray A 0.3/0.5/1.2 (4)

## Slide 14: Topic 2: future directions?
Multiple injections
  IFPEN 2009