## Slide 1: Spray G Modeling
ECN 3.0
April 5th, 2014

## Slide 2
Participating Institution | Abbreviation | Researcher(s)
Argonne National Lab | ANL | Zihan Wang, Sibendu Som
Politecnico di Milano | Polimi | Tommaso Lucchini, Tarcisio Cerri
University of Wisconsin – Madison | UW | Noah Van Dam

## Slide 3: Modeling Outline
Case description
Modeling approaches
CFD Measurement definitions
Modeling results
  Liquid and vapor penetration
  Spray visualization
  Mixture fraction and drop size (SMD) profiles
Summary

## Slide 4: Spray G Nominal Baseline Data/Conditions
Fuel | Isooctane
Injection Pressure | 20 MPa
Fuel Temperature | 90° C (363.15 K)
Ambient Temperature | 300° C (573.15 K)
Ambient Density | 3.5 kg/m3
- Ambient Pressure | 5.97 bar (N2); 5.77 bar (Air)
Injected Quantity | 10 mg
Injection Duration | 780 µs
Number of Nozzle Holes | 8
Hole Diameter | 165 µm
Fully Included Angle | 80°

## Slide 5: Rate of Injection
Chart: Time (ms)

## Slide 6: Modeling Approaches
 | ANL | Polimi | UW
CFD Code | Converge 2.1.0 | OpenFOAM + Lib-ICE | KIVA3V-r2-ERC
Turbulence Model | Standard k-ε | Standard k-ε | RNG k-ε
Injection Model | Lagrangian/Blob | Lagrangian/Huh | Lagrangian/Blob
Primary Break-up Model | KH-RT (B1 7; RT Length 0.0) | Huh-Gosman | KH-RT (B1 40; RT Length 1.0)
Secondary Break-up |  | Wave | 
Vaporization | Frössling | Spalding Number-based (mass-based) | Frössling
Heat Transfer | O’Rourke | Ranz-Marshall | Ranz-Marshall
Collision | NTC | None | 
Turbulent Dispersion | O’Rourke | None | Gaussian Distribution
Droplet Drag | Dynamic | Dynamic w/ non-spherical correction | Dynamic w/ non-spherical correction

## Slide 7: Mesh Details
 | ANL | Polimi | UW
Domain Dimensions | 108 Ø x 108 mm | 169 x 248 mm | 100 x 100 x 60 mm
Base Cell Size | 2 mm | 4 mm | 1 mm
Min Cell Size | 0.25 mm | 1 mm | -
Adaptive or Static Refinement | Both | Adaptive | Uniform
Cell Type | Cartesian | Cartesian | Cartesian Hexahedron
Total/Maximum Cell Count | 1.53 Million | 115,000 | 600,000

## Slide 8: CFD Penetration Measurement Details
Liquid Penetration
  0.1 % Liquid volume fraction threshold
Vapor Penetration
  0.1 % Mixture fraction threshold
Measured along injector axis
  Zero point at injector tip
Penetration
Length
Side View

## Slide 9: Mixture Fraction and SMD Profile Locations
Spray Axis
  Along centerline of a spray jet
Injector Axis
  Along the injector axis
Radial
  Radially through spray jet center point in a plane 15 mm downstream
Transverse
  Perpendicular to radial profile through spray jet center point in a plane 15 mm downstream
Dual-plume
  On a line connecting the center points of two neighboring spray jets in a plane 15 mm downstream

## Slide 10: Profile Location – Spray Axis
Along the centerline of an individual spray jet
  Distanced measure along the spray axis
    Zero at injection location, positive towards spray tip
Profile Line
Profile Line
Top View
Side View

## Slide 11: Profile Location – Injector Axis
Along the injector axis
  Distance measure along the injector axis
    Zero at nozzle tip, positive towards leading edge
Profile Line
Top View
Side View

## Slide 12: Cross-section Plane
15 mm
Plane normal to injector axis
Located 15 mm downstream of injector tip measured along injector axis
Side View
Top View

## Slide 13: Radial Cross-section
Along a radial line through the spray axis center point
  Zero at injector axis, positive outward
Radial Line
15 mm
Side View
Top View

## Slide 14: Transverse Cross-section
Across the spray perpendicular to the radial line
  Zero at spray center point
    Experiments put this at 10 mm radial distance
  Positive direction clockwise as viewed from injector
15 mm
Side View
10 mm
Spray Plume Center
Transverse Line
Top View

## Slide 15: Dual-plume Cross-section
Taken along a line connecting the center-points of two neighboring spray plumes
  Zero at center of counter-clockwise-most (as viewed from injector) plume
  Positive towards second plume (clockwise as viewed from injector)
Dual-plume Line
15 mm
Side View
Top View

## Slide 16: Image View Orientations
Camera/Viewing Position
Position 1 (Widest Spray)
Position 2 (Narrowest Spray)

## Slide 17: Spray Penetration
Liquid Penetration
Vapor Penetration

## Slide 18: Spray Penetration (Initial Transient)
Liquid Penetration
Vapor Penetration

## Slide 19: Liquid Images – View 1
0.3 ms ASOI
Experiment
Polimi
ANL
UW

## Slide 20: Liquid Images – View 1
0.5 ms ASOI
Experiment
Polimi
ANL
UW

## Slide 21: Liquid Images – View 1
0.7 ms ASOI
Experiment
Polimi
ANL
UW

## Slide 22: Liquid Images – View 1
0.9 ms ASOI
Experiment
Polimi
ANL
UW

## Slide 23: Vapor Images – View 1
0.3 ms ASOI
Experiment
Polimi
ANL
UW

## Slide 24: Vapor Images – View 1
0.5 ms ASOI
Experiment
Polimi
ANL
UW

## Slide 25: Vapor Images – View 1
0.7 ms ASOI
Experiment
Polimi
ANL
UW

## Slide 26: Vapor Images – View 1
0.9 ms ASOI
Experiment
Polimi
ANL
UW

## Slide 27: Vapor Images – View 1
1.5 ms ASOI
Experiment
Polimi
ANL
UW

## Slide 28: Mixture Fraction Profile – Spray Axis
0.6 ms ASOI
1.0 ms ASOI
1.4 ms ASOI

## Slide 29: Mixture Fraction Profile – Injector Axis
0.6 ms ASOI
1.0 ms ASOI
1.4 ms ASOI

## Slide 30: Mixture Fraction Profile – Radial Profile
0.6 ms ASOI
1.0 ms ASOI
1.4 ms ASOI

## Slide 31: Mixture Fraction Profile – Transverse Profile
0.6 ms ASOI
1.0 ms ASOI
1.4 ms ASOI

## Slide 32: Mixture Fraction Profile – Dual-plume Profile
0.6 ms ASOI
1.0 ms ASOI
1.4 ms ASOI

## Slide 33: SMD Profile – Radial Profile
0.6 ms ASOI
1.0 ms ASOI
1.4 ms ASOI

## Slide 34: SMD Profile – Transverse Profile
0.6 ms ASOI
1.0 ms ASOI
1.4 ms ASOI

## Slide 35: SMD Profile – Dual-plume Profile
0.6 ms ASOI
1.0 ms ASOI
1.4 ms ASOI

## Slide 36: Summary
Penetration all similar to experimental data
  Initial transients should be investigated more
  Liquid vaporization time incorrect?
Best practice to compare liquid images?
Upstream (near-nozzle) vapor behavior, detached or not?
Some simulations may be under-resolved

## Slide 37: Future Work
More accurate boundary conditions from experiments
  Hole specific boundary conditions?
Parametric variations
Better ways to understand spray-to-spray interactions

## Slide 39: Mixture Fraction Profile – Spray Axis
0.6 ms ASOI

## Slide 40: Mixture Fraction Profile – Spray Axis
0.8 ms ASOI

## Slide 41: Mixture Fraction Profile – Spray Axis
1.0 ms ASOI

## Slide 42: Mixture Fraction Profile – Spray Axis
1.2 ms ASOI

## Slide 43: Mixture Fraction Profile – Spray Axis
1.4 ms ASOI

## Slide 44: Mixture Fraction Profile – Injector Axis
0.6 ms ASOI

## Slide 45: Mixture Fraction Profile – Injector Axis
0.8 ms ASOI

## Slide 46: Mixture Fraction Profile – Injector Axis
1.0 ms ASOI

## Slide 47: Mixture Fraction Profile – Injector Axis
1.2 ms ASOI

## Slide 48: Mixture Fraction Profile – Injector Axis
1.4 ms ASOI

## Slide 49: Mixture Fraction Profile – Radial Profile
0.6 ms ASOI

## Slide 50: Mixture Fraction Profile – Radial Profile
0.8 ms ASOI

## Slide 51: Mixture Fraction Profile – Radial Profile
1.0 ms ASOI

## Slide 52: Mixture Fraction Profile – Radial Profile
1.2 ms ASOI

## Slide 53: Mixture Fraction Profile – Radial Profile
1.4 ms ASOI

## Slide 54: Mixture Fraction Profile – Transverse Profile
0.6 ms ASOI

## Slide 55: Mixture Fraction Profile – Transverse Profile
0.8 ms ASOI

## Slide 56: Mixture Fraction Profile – Transverse Profile
1.0 ms ASOI

## Slide 57: Mixture Fraction Profile – Transverse Profile
1.2 ms ASOI

## Slide 58: Mixture Fraction Profile – Transverse Profile
1.4 ms ASOI

## Slide 59: Mixture Fraction Profile – Dual-plume Profile
0.6 ms ASOI

## Slide 60: Mixture Fraction Profile – Dual-plume Profile
0.8 ms ASOI

## Slide 61: Mixture Fraction Profile – Dual-plume Profile
1.0 ms ASOI

## Slide 62: Mixture Fraction Profile – Dual-plume Profile
1.4 ms ASOI

## Slide 63: Mixture Fraction Profile – Dual-plume Profile
0.6 ms ASOI

## Slide 64: SMD Profile – Radial Profile
0.6 ms ASOI

## Slide 65: SMD Profile – Radial Profile
0.8 ms ASOI

## Slide 66: SMD Profile – Radial Profile
1.0 ms ASOI

## Slide 67: SMD Profile – Radial Profile
1.2 ms ASOI

## Slide 68: SMD Profile – Radial Profile
1.4 ms ASOI

## Slide 69: SMD Profile – Transverse Profile
0.6 ms ASOI

## Slide 70: SMD Profile – Transverse Profile
0.8 ms ASOI

## Slide 71: SMD Profile – Transverse Profile
1.0 ms ASOI

## Slide 72: SMD Profile – Transverse Profile
1.2 ms ASOI

## Slide 73: SMD Profile – Transverse Profile
1.4 ms ASOI

## Slide 74: SMD Profile – Dual-plume Profile
0.6 ms ASOI

## Slide 75: SMD Profile – Dual-plume Profile
0.8 ms ASOI

## Slide 76: SMD Profile – Dual-plume Profile
1.0 ms ASOI

## Slide 77: SMD Profile – Dual-plume Profile
1.2 ms ASOI

## Slide 78: SMD Profile – Dual-plume Profile
1.4 ms ASOI